## Slide 1: Introduction to Telecommunications
Prof. Andrzej Jajszczyk
2020/2021

## Slide 2: Course
Lectures: Andrzej Jajszczyk Available: D-6/room 406, jajszcz@agh.edu.pl Mondays: 14:30 – 16:00
Exercises (Zbigniew Hulicki)
Final mark:
* all marks need to be 3.0 or higher

## Slide 3: Info
E-mail: jajszcz@agh.edu.pl
Personal web page: http://new.kt.agh.edu.pl/en/user/148
Slides: Teams, Introduction to Telecommunications

## Slide 4: Lecture Topics
Scope of telecommunications
Essential notions, units, and limits
Services and terminals
Transmission media
Signal transmission
Signal coding
Key networking issues

## Slide 5: Lecture Topics
Switching and routing
Traffic engineering
Wireless networking
Transmission systems
Network and service management
Legal, economic, and standardization issues in telecommunications
Telecommunications and environment

## Slide 6: Exercises
Wiring the RJ-45 connectors
Logarithmic scale in telecommunications, decibels
Telecommunication traffic
Basic network commands for Windows and Linux systems
Techniques and network protocols, Wireshark
Coding of signals in telecommunications

## Slide 7: References
Slides
Books
Journals
  IEEE Communications Magazine
  Przegląd Telekomunikacyjny i Wiadomości Telekomunikacyjne
WWW documents

## Slide 8
http://ieeexplore.ieee.org/

## Slide 9
http://dl.acm.org/

## Slide 10
http://scholar.google.pl/

## Slide 11: Scope of Telecommunications
Outline
Notion of telecommunications
Milestones (S. Morse, A. G. Bell, and others)
Culture groups
Areas of telecommunications (services, transmission, switching, management,...)
OSI/ISO model, physical layer model
Conclusion

## Slide 12: Telecommunications
From Latin: communicatio = exchange, talk
From Greek: tele = distant
Telecommunications means information exchange between distant points
Notes: Telecommunication is communication at a distance by technological means, particularly means based on electrical signals or electromagnetic waves.

## Slide 13: 1837: Invention of the Telegraph
Samuel Morse
Notes: He used magnetism to create electromagnetic telegraph. Then he created a special set of codes (based on a dictionary) used to transmit information. He was the first to patent the telegraph, however, he was not the first person in the World to create the invention.
Kod Morse’a został wymyślony przez Alfreda Vaila.

## Slide 14: Samuel Morse

## Slide 15: 1876: Invention of the Telephone
Alexander Graham Bell
Notes: He worked with deaf people and created a model of a microphone and a speaker. However, they were too big to be carried by deaf people. He connected both of them and created a telephone.
He established Bell Telephone Company which turned later into AT&T – the largest telecom company in the World. Also he established a set of laboratories which changed their name to Bell Laboratories after his death.
1857 – Antonio Meucci skonstruował prototyp telefonu, ale go nie opatentował.
1876 – Aleksander Graham Bell opatentował telefon elektryczny.

## Slide 17: Three Culture Groups
Telecommunications
Computer networking
Media (content providers)

## Slide 18: Convergence of Parameters
Flexibility
Quality of Service
Bandwidth
Internet
CATV
PSTN

## Slide 19: Areas of Telecommunications
Services
Transmission
Switching
Management
etc.

## Slide 20: Models of Communications Systems
Layered models
Signal model (physical layer)

## Slide 21: Example of a Simple Communications Architecture
Typical tasks to be performed to send a file between computers:
System 1 has to notify the network about the required destination
System 1 has to check if System 2 is ready to accept data
A file transfer application in System 1 has to check if the file management program in System 2 is ready to receive and store a file from a given user
If file formats in both systems are different, one of the systems has to convert the format
Telecommunications
network
System 1
System 2

## Slide 22: Simple File Transfer Architecture
System 1
System 2
Files and file transfer commands
Network interface
Communications messages
Network
Communications module
File transfer application
Access module
Communications module
File transfer application
Access module

## Slide 23: Protocols in Example Layered Architecture
System 1
System 2
Application protocol
Transport protocol
Network access protocol
Network
Transport
Applications
Network access
Transport
Applications
Network access

## Slide 24: System “Chef” Sent Letters
Buy ingredients: eggs, butter, salt, pepper...
Take bowl: scramble eggs, add salt ...
Take pan:
melt butter,
add eggs...

## Slide 25: System “Chef” Received Letters
Buy ingredients: eggs, butter, salt, pepper...
Take bowl: scramble eggs, add salt ...
Take pan:
melt butter,
add eggs...

## Slide 26: System “Chef” Numbered Letters
1/3
Buy ingredients: eggs, butter, salt, pepper...
2/3
Take bowl: scramble eggs, add salt ...
3/3
Take pan:
melt butter,
add eggs...

## Slide 27: System “Chef” Lost Letter
1/3
Buy ingredients: eggs, butter, salt, pepper...
3/3
Take pan:
melt butter,
add eggs...

## Slide 28: Layered Architecture of System “Chef”
Kitchen 1
Kitchen 2
Application protocol (“Chef”)
“Secretary” protocol
“Post Office” protocol
Post office
Handling
of envelopes
and messages
Applications
Mailing
and receiving letters
Handling
of envelopes
and messages
Applications
Mailing
and receiving letters

## Slide 29: OSI model
OSI Open System Interconnection
The OSI model is an attempt to provide an international standard framework that describes the complete network protocol stack in heterogeneous computer network environments
ISO 7498 Standard
ITU-T X.200 Recommendation
Notes: Wg. Y. Zheng, S. Akhtar, Networks for Computer Scientists and Engineers, Oxford Univ. Press, 2002

## Slide 30: Defining OSI Layers (1)
Do not create too many layers to simplify layer description and integration
Create layer boundary at the point where service description is simple and the number of interactions across it is minimal
Separate layers should be created for functions that are clearly different in terms of related processes or technologies
Similar functions should be gathered in the same layer
Boundaries should be selected at points where they proved themselves previously

## Slide 31: Defining OSI Layers (2)
A layer should be defined in such a way that it can be entirely re-designed and its protocols replaced without changing services offered to neighboring layers
A layer should be created where a different abstraction level in data handling is required (e.g., morphology, syntax, semantics)
Modification of functions and protocols within a layer should not impact other layers
Layer boundaries should be defined exclusively with layers directly above or below a given layer

## Slide 32: The OSI Seven-Layer Model
Physical medium
Protocols
Application
Application
7
Presentation
Presentation
6
Session
Session
5
Transport
Transport
4
Network
Network
3
Data link
Data link
2
Physical
Physical
1

## Slide 33: The OSI Seven-Layer Model: Layer 1
Binary transmission:
Mechanical interface to the transmission medium (e.g., the number of pins in a plug)
Electrical interface (e.g., voltage related to logical “1”)
Procedural interface (e.g., how to activate a connection)
Data unit: bit
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 34: The OSI Seven-Layer Model: Layer 2
Link control, medium access control:
Error free transmission of signals between two nodes
Retransmission of frames containing errors
Error detecting and correcting coding
Transmission unit: frames
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 35: The OSI Seven-Layer Model: Layer 3
Addressing and best path selection:
Logical addresses
Choosing the best path
Connectionless data transfer
No error detection or correction
Transmission unit: packet (datagram)
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 36: The OSI Seven-Layer Model: Layer 4
End-to-end data transfer:
Transmission control
Reliable services using unreliable network services
  error detection
  retransmissions
  packet ordering
Quality of Service (QoS)
Transmission unit: segments
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 37: The OSI Seven-Layer Model: Layer 5
The session layer takes care of a dialogue between two applications:
Opening and closing sessions between applications
Session management
Three types of dialogue
  Two-way duplex
  Two-way half-duplex
  Simplex
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 38: The OSI Seven-Layer Model: Layer 6
Representation of data:
  Character code conversion
  Data ciphering and deciphering
  Data compression and decompression
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 39: The OSI Seven-Layer Model: Layer 7
Provision the user interface for the network
Examples
  File transfer
  Data base access
  Virtual terminal
Application
Presentation
Session
Transport
Network
Data link
Physical
6.
7.
5.
4.
3.
2.
1.

## Slide 40: The OSI Seven-Layer Model
Physical medium
Application
Application
7
Presentation
Presentation
6
Session
Session
5
Transport
Transport
4
Network
Network
3
Data link
Data link
2
Physical
Physical
1
01000110101101000100101
Data stream
Data stream
Data stream
Data
Data
Data
Data
Packet
header
Data
Packet
header
Frame
header

## Slide 41: Layer Protocol Examples
Application
7
Presentation
6
Session
5
Transport
4
Network
3
Data link
2
Physical
1
FTP, SMTP, HTTP
ASCII, SSL
sockets
TCP, UDP
IP, IPSec, ICMP, IGMP, OSPF,
Ethernet, 802.11 a/b/g/n MAC/LLC
RJ45, RS-232, STP, DSL
Notes: SMTP – Simple Mail Transfer Protocol
HTTP – HyperText Transfer Protocol

## Slide 42: Communications System (Physical Layer) Model
Receiver
Source
Channel
Sender
Source coder
Channel coder
Modulator
Demodulator
Destination
Source decoder
Channel decoder
Noise

## Slide 43: Conclusion
Notion of telecommunications
Milestones (S. Morse, A. G. Bell, and others)
Culture groups
Areas of telecommunications (services, transmission, switching, management,...)
OSI/ISO model

## Slide 44
Thank you very much for your attention