## Slide 1: Transmission Media
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 4

## Slide 2: Outline
Introduction
Copper cables in telecommunications and computer networking
Fiber-optic cables
Wireless transmission
Conclusion

## Slide 3: Copper Cables
Speed of light in vacuum:
300 000 km/s
Speed of electron movement in a conductor (DC source):
 1 m/h
Speed of current flow in a copper wire:
 200 000 km/s

## Slide 4: Newton’s Cradle

## Slide 5: Twisted Pair
Twisted pair
+
–
+
–
Differential receiver
Differential transmitter
Noise

## Slide 6: Computer Networking Cables
Types:
  UTP Unshielded Twisted Pair
  FTP Foil screened Twisted Pair
  STP Shielded Twisted Pair
Categories:
  1 and 2: audio systems
  3: 16 MHz – up to 10 Mbit/s
  4: 20 MHz – up to 20 Mbit/s
  5: 100 MHz – up to 1000 Mbit/s
  6: 250 (500) MHz – up to 10 Gbit/s
  7: 600 MHz – 10 Gbit/s and more

## Slide 7: Optical Fiber Structure
Core
Cladding
Primary coating (plastic)
5 – 62.5
μ
m
125
μ
m
245
μ
m
Core of pure glass
Cladding of glass of a lower refractive index than the core

## Slide 8: Principle of Operation
Core
Cladding
Optical fibers operate by using the total internal reflection

## Slide 9: A Little Bit of Physics
Air (n1)
Water (n2)
Incident ray
Refracted ray
(strong)
Reflected ray
(weak)

## Slide 10: A Little Bit of Physics (2)
Air (n1)
Water (n2)
Incident ray
Refracted ray
(weak)
Reflected ray
(strong)

## Slide 11: Total Internal Reflection
Air (n1)
Water (n2)
Incident ray
No refracted ray!
Reflected ray
(100% power)
Total Internal Reflection causes 100% reflection

## Slide 12: Attenuation vs. Wavelength
Wavelength
[
µ
m
]
0
.
7
0
.
8
0
.
9
1
.
0
1
.
1
1
.
2
1
.
3
1
.
4
1
.
5
1
.
6
1
.
7
1
.
8
1
.
9
2
.
0
1
2
3
4
Loss
[
d
B
/
k
m
]
Attenuation
First window
Second window
Third window (C band)
Fourth window (L band)
Notes: Each wavelength produces different characteristics in terms of: attenuation, dispersion and other non-linear distortions.
Each effect that contributes to attenuation and dispersion depends on the optical wavelength. The wavelength bands (or windows) that exist where these effects are weakest are the most favorable for transmission. These windows have been standardized, and the currently defined bands are the following.
Historically, there was a window used below the O band, called the first window, at 800-900 nm; however, losses are high in this region so this window is used primarily for short-distance communications.

## Slide 13: Transmission Windows
Band | Description | Wavelength Range
O band | original | 1260 to 1360 nm
E band | extended | 1360 to 1460 nm
S band | short wavelengths | 1460 to 1530 nm
C band | conventional ("erbium window") | 1530 to 1565 nm
L band | long wavelengths | 1565 to 1625 nm
U band | ultralong wavelengths | 1625 to 1675 nm
Current technology has managed to combine the second and third windows that were originally disjoint
The first window at 800-900 nm remained historically for short-distance communications

## Slide 14: Optical Fiber Capabilities
24 fibers
By using a DWDM system, bit rates of 2.4 Tbit/s can be achieved, what allows:
  38 million simultaneous telephone calls
  Transfer of 70 000 volumes of encyclopedia per second
A typical optical cable
Manufacturer: Tele-Fonika

## Slide 15: Cross-Section of an Optical Cable
Manufacturer: Tele-Fonika
Stranding steel wire
Inner buffer tube
Thixotropic gel
Optical fiber
Outer jacket
Hot melt (filling compound)
Ripcord (for jacket removal)
Wrapping tape
Dielectric strength member

## Slide 16: James C. Maxwell (1831-1879)
1873: Publication of Treatise on Electricity and Magnetism devoted to electromagnetic phenomena. By using a purely mathematical reasoning, Maxwell presents in a single formula set basic relations between electricity and magnetism. He suggests the existence of various kinds of electromagnetic radiation, propagating at the speed of light

## Slide 17: Electromagnetic Waves

## Slide 18: Maxwell's Equations
The author of Maxwell’s Equations as above is:
Oliver Heaviside
The Divergence Operator
The Curl Operator
D: The Electric Flux Density
: The Electric Charge Density
B: The Magnetic Flux Density
E: The Electric Field,
H: The Magnetic Field
J: The Electric Current Density

## Slide 19: Heinrich Hertz (1857-94)
1888: Heinrich Hertz, Professor of physics at Polytechnic in Karlsruhe, Germany, conducts an experiment confirming the existence of electromagnetic waves, as predicted by Maxwell. Hertz confirms also that the radio waves propagate at the speed of light
Notes: He studied Maxwell’s theory and conduicted experiments later on.

## Slide 20: Radio Inventors
Maholm Loomis (1866) Early experiments in Virginia, USA
Nicola Tesla (1893) Demonstrated a small radio-controlled boat Before invention of motor vehicles and radio!
Alexander Popow (1896)
Guglielmo Marconi (1896)
  1897: Marconi Wireless Telegraph Company established
  1901: letter “s” sent across Atlantic
  1909: Nobel Prize in Physics
Notes: letter ‘s’ in Morse code sent from Canada to England
Konkurentami do tytułu wynalazcy byli także serbski inżynier i wynalazca Nikola Tesla oraz rosyjski fizyk Aleksandr Popow. W 1943 Sąd Najwyższy Stanów Zjednoczonych przyznał prawa patentowe Tesli[1]. Rozprawa rozstrzygnęła się po śmierci wynalazcy, przez co powszechnie za twórcę radia uznaje się Marconiego, mimo iż przyznał się on do wykorzystania wcześniejszych prac Tesli w zbudowaniu radia.
Tesla opracował konstrukcję cewki wysokonapięciowej, wysyłającej silne fale elektromagnetyczne i zaczął pracować nad urządzeniem, które mogłoby te fale odbierać. Jego patent na urządzenie do przesyłania i odbioru fal elektromagnetycznych był gotowy w 1900 roku, jednak ubiegł go w tym o kilka dni Marconi. Tesla walczył z Marconim o patent na radio, dowodząc, że jego wynalazek stosuje bez jego zgody wcześniej opatentowaną przez siebie cewkę, ale długie procesowanie się doprowadziło Teslę do bankructwa. Ostatecznie dobił go fakt przyznania Marconiemu nagrody Nobla za skonstruowanie radia, mimo iż korzystał on przy tym z teorii stworzonych przez Teslę. Ironią losu jest to, że ostatecznie odwołanie Nikoli Tesli w sprawie patentu na radio do sądu najwyższego USA zostało wygrane już po jego śmierci w 1943 roku.

## Slide 21: Laurent Montaron, The Invisible Message, 2011

## Slide 22: Useful Ranges of Radio Waves
Around 100 kHz: electromagnetic energy is guided around the Earth
1 MHz – 30 MHz: energy begins to travel in straight lines and is reflected by the ionosphere
Above 50 MHz: energy propagates in straight lines and is not reflected by the ionosphere
Above 10 GHz: intense rainfall considerably attenuates signals
Above 20 GHz: water and oxygen molecules in the atmosphere become significant energy absorbers; communication is limited to windows between the absorption bands
Notes: Above 10 GHz: Satellite TV
Above 50 Mhz: Typical Radio UHF

## Slide 23: Arthur C. Clarke
1945 Arthur C. Clarke published an article in Wireless World entitled: “Extra-Terrestrial Relays” presenting the concept of geostationary satellites and their usage for communications.
'An artificial satellite at the correct distance from the earth could make one revolution every 24 hours, i.e., it would remain stationary above the same spot and would be within optical range of nearly half of the earth's surface. Three repeater stations, 120 degrees apart in the correct orbit could give television and microwave coverage to the entire planet.'
Notes: 2001: A Space Odyssey, 1968
W wielu opracowaniach technicznych orbita geostacjonarna nosi nazwę "orbity Clarka".
Wielu naukowców uważało Clarka za fantastę, a jego wizję za utopię. Jednak 12 lat później pierwszy sztuczny satelita ziemi, sowiecki Sputnik, rozpoczął nadawanie sygnałów radiowych z kosmosu.

## Slide 25: Geostationary Earth Orbit (GEO) Satellites (2)
Earth
Distance from Earth: 35 786 km above equator
Earth radius: 6370 km
17.4
Notes: Above equator!

## Slide 26: Geostationary Earth Orbit (GEO) Satellites (3)
Question 1:
What is the delay of the signal on the path: Earth-Satellite-Earth?
Answer:
Therefore:
The delay of typical communication between two earthbound stations via satellites reaches 0.5 s

## Slide 27: Geostationary Earth Orbit (GEO) Satellites (4)
Question 2:
What is the linear speed of the satellite (let us assume that Earth does not revolve around the sun)
Answer:

## Slide 28: Types of Satellite Orbits
LEO
MEO
GEO
HEO
LEO: Low Earth Orbit
MEO: Medium Earth Orbits
GEO: Geostationary Earth Orbit
HEO: Highly Elliptical Orbit
Notes: LEO: Low Earth Orbit
MEO: Medium Earth Orbits
GEO: Geostationary Earth Orbit
HEO: Highly Elliptical Orbit

## Slide 29: Commercial Communications Geostationary Satellites

## Slide 30: GPS: Global Positioning System
24 (now 31) satellites in six circular orbital planes. The orbits are arranged so that at least four satellites are always within line of sight from almost everywhere on Earth's surface.
Altitude of approximately 20 183 km
Notes: 28 satellites are always opperational. The rest can be under tests or technical off-cycles.
NUDET – Nuclear Detection mechanism (installed on every satellite) - immediately detects nuclear explosions on the Earth.

## Slide 31: GPS Constellation in Motion

## Slide 32: Low-orbit Satellites
Irydium (Motorola) 66 satellites (originally 77)
Globalstar (Qualcomm) 48 satellites
SkyBridge (Alcatel) 80 satellites
SkyBridge
Notes: System, zbudowany przez Motorolę za 5 G$, sprzedano za 25 M$. Iridium Satellite LLC zredukowało koszty utrzymania systemu, z 12 adapterów międzysieciowych pozostał jeden. Firma ma stały kontrakt z Departamentem Obrony USA na 20 tys. użytkowników sieci. Poza tym, zamierza świadczyć usługi głównie firmom, dla których łączność satelitarna jest niezbędna (transport morski, lotnictwo), oraz organizacjom pozarządowym.

## Slide 33: Stratospheric Platforms
SkyNet
Multimedia services
Broadband Internet
Fast WAN
Complex services
Advanced PCS systems
Advanced terminals
Access links

## Slide 34: Conclusion
Copper cables in telecommunications and computer networking
Fiber-optic cables
Wireless transmission

## Slide 35: Thank you very much for your attention