## Slide 1: Legal, Economic, and Standardization Issues in Telecommunications
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 13

## Slide 2: Outline
Introduction
Types of Telecommunication Companies
Regulation
Standardization in telecommunications
  ITU-T
  European standards organizations
  IETF vs. other standards organizations
Net Neutrality
Conclusion

## Slide 3: Traditional Types of Telecommunication Companies
Network Provider
Service Provider
Content Provider

## Slide 4: New Types
ASP (Application Service Provider)
ISP (Internet Service Provider)
NSP (Network Service Provider)
Carriers
Carriers’ Carrier
Notes: A network service provider (NSP) is a company that provides backbone services to an Internet service provider (ISP), the company that most Web users use for access to the Internet.
A carrier's carrier is a telecommunications industry business model where a carrier sells or leases bandwidth on its own infrastructure to another telecom carrier for reselling to their own customers.

## Slide 5: Dependencies
Telecommunications infrastructure
Value added services
Global or inter-regional transport network
ISP
ASP
NSP

## Slide 6: Need for Regulatory Intervention
Breaking telecommunication monopolies
Increasing competition within the telecommunication market
Authorization or licensing new operators
Removing barriers to market entry by new operators
Overseeing interconnection of new entrants with incumbent operators
Ensuring competitive markets do not fail to serve high cost areas or low income subscribers

## Slide 7: Widely Accepted Regulatory Objectives
Promote universal access to basic telecommunications services
Foster competitive markets to promote:
  efficient supply of telecommunications services
  good quality of service
  advanced services
  efficient prices
Where competitive markets do not exist or fail, prevent abuses of market power such as excessive pricing and anti-competitive behavior by dominant firms
Source: Telecommunications Regulation Handbook, The World Bank, 2000, USA

## Slide 8: Widely Accepted Regulatory Objectives (2)
Create a favorable climate to promote investment to expand telecommunications networks
Promote public confidence in telecommunications markets through transparent regulatory and licensing processes
Protect consumer rights, including privacy rights
Promote increased telecommunications connectivity for all users through efficient interconnection arrangements
Optimize use of scarce resources, such as the radio spectrum, numbers and rights of way
Source: Telecommunications Regulation Handbook, The World Bank, 2000, USA

## Slide 9: Standard Institutional Structure in Developed Market Economies
Function | Responsible Organization
Policy Development | Government Ministry or Executive Branch
Regulation | Separate Regulatory Authority
Network Operations/Service Provision | Public Telecommunications Operators (privately or commercially operated)

## Slide 10: Standardization
The nice thing about standards is that there are so many of them to choose from
Andrew S. Tanenbaum
International standards organizations
ITU (International Telecommunication Union)
  ITU-T (to 1993: CCITT, Comité Consultatif International Télégraphique et Téléphonique)
  ITU-R (to 1993: CCIR, Comité Consultatif International des Radiocommunications)
ISO (International Standards Organisation)
CEI (Commission Électrotechnique Internationale)
IEEE (The Institute of Electrical and Electronics Engineers)
IETF
others
Notes: ITU jest organizacją międzyrządową z siedzibą w Genewie. Jej członkiem może zostać państwo należące do ONZ. ITU spełnia trzy podstawowe funkcje: standaryzacyjną, regulacyjną (głównie w zakresie radiokomunikacji) i związaną z rozwojem telekomunikacji w ogólności.
ITU-T (ITU-Telecommunications Standardization Sector) jest agendą ITU odpowiedzialną za standaryzację w dziedzinie telekomunikacji. Prace standaryzacyjne odbywają się w Grupach Studiów (ang. Study Group). Każda z grup zajmuje się pewnym obszarem telekomunikacji (transmisja, komutacja, utrzymanie itd.). Obecnie istnieje 15 Grup Studiów. Ich członkami są delegaci mianowani przez poszczególne Administracje reprezentujące rządy krajów członkowskich ITU. Inne organizacje (np. operatorzy, producenci czy organizacje użytkowników) mogą również brać udział w pracach standaryzacyjnych wysyłając swoich ekspertów pod warunkiem, że uzyskają zgodę swojej narodowej administracji.
W pracach Grupy Studiów może uczestniczyć nawet ponad 400 osób. Dlatego też dzieli się ją na Grupy Robocze (ang. Working Parties), z których każda zajmuje się pewną cześcią zadań. Grupy Robocze mogą być, zależnie od potrzeb, dzielone np. na zespoły ekspertów, czy zwoływane ad hoc podgrupy.
Każdy standard opracowany przez Grupę Studiów musi być jednomyślnie zatwierdzony przez Administracje. Do 1988 wstępne wersje standardów musiały być zatwierdzane przez Zgromadzenie Ogólne CCITT, zbierające się raz na cztery lata. Obecnie coraz częściej stosuje się “procedurę przyspieszoną”, w której wstępne wersje standardów po jednomyślnym zatwierdzeniu przez Administracje na spotkaniu odpowiedniej Grupy Roboczej są ostatecznie zatwierdzane drogą korespondencyjną. Wymagana jest przy tym większość 80% głosów pozytywnych.
Standardy opracowywane przez ITU-T noszą nazwę zaleceń (ang. recommendations) dla podkreślenia dobrowolności ich wykorzystywania (jakkolwiek zalecenia ITU-T mają w rzeczywistości znaczenie standardów i trudno by było sobie wyobrazić współpracę różnych sieci bez ich przestrzegania).

## Slide 11: ITU: Selected Study Groups
SG 2: Service definition, numbering and routing
SG 4: Telecommunication management
SG 9: Integrated broadband cable and TV networks
SG 11: Intelligent networks
SG 12: Quality of service and performance
SG 13: NGN and satellite matters
SG 15: Optical and other transport network infrastructures
SG 16: Multimedia terminals, systems and applications; Ubiquitous applications (“e-everything”, such as e-health and e-business)
SG 17: Telecommunication security; languages and description techniques
SG 19: Mobile telecommunication networks

## Slide 12: ITU-T Recommendation Series
Series A Organization of the work of the ITU-T
Series B Means of expression
Series C General telecommunication statistics
Series D General tariff principles
Series E Telephone network and ISDN
Series F Non-telephone telecommunication services
Series G Transmission systems and media
Series H Transmission of non-telephone signals
Series I Integrated services digital network
Series J Transmission of sound-programme and television signals
Series K Protection against interference
Series L Construction, installation and protection of cables and other elements of outside plant

## Slide 13: ITU-T Recommendation Series
Series M Maintenance: international transmission systems, telephone circuits, telegraphy, facsimile
Series N Maintenance: international sound- programme and television transmission circuits
Series O Specifications of measuring equipment
Series P Telephone transmission quality
Series Q Switching and signalling
Series R Telegraph transmission
Series S Telegraph services terminal equipment
Series T Terminal equipments and protocols for telematic services
Series U Telegraph switching
Series V Data commun. over the telephone network
Series X Data networks and open system communications
Series Z Programming languages

## Slide 14: ITU-T: Approval Process (Accelerated Procedure)
4
(b)
(c)
9
11
(a)
(a)
(b)
(a)
(b)
SG or
WP
meeting
(
1
)
Edited
text
for LC
(
2
)
Director's
announcement
and posting
for LC
(
3
)
Edited
text
for AR
(
8
)
Director's
announcement
and posting
for AR
(
10
)
Director's
announcement
and posting
(
5
)
SG
Meeting
(
6
)
Director's
notification
and publication
(
12
)
3 weeks
LC: Last Call
AR: Additional Review
Approved
Approved
Approved
Comment
resolution
(7)
AR
3 weeks
LC
4 weeks
SG: Study Group
WP: Working Party

## Slide 15: European Standardization Bodies
ETSI (European Telecommunication Standards Institute)
CEN (Comité Européen de Normalisation)
CENELEC (Comité Européen de Normalisation Électrotechnique)
ECMA (European Computer Manufacturers Association)
EWOS (European Workshop on Open Systems)
Notes: ETSI zostało utworzone w 1988 roku z inicjatywy Komisji Europejskiej w celu sharmonizowania wysiłków w całym obszarze telekomunikacji oraz, we współpracy z innymi organizacjami standaryzacyjnymi, w obszarze technik rozgłoszeniowych i biurowej technologii informacyjnej.
Zadaniem ETSI jest opracowywanie wspólnych standardów dla Europy umożliwiających łączenie sieci i wymianę usług oraz zapewniających współpracę sprzętu w skali europejskiej. Poprzez uwzględnienie postepu w tej dziedzinie w skali globalnej ETSI bierze udział w tworzeniu standardów telekomunikacyjnych o zasięgu światowym.
ETSI jest organizacją niezależną i samofinansującą. Członkami ETSI mogą być użytkownicy, operatorzy sieci publicznych, producenci, dostarczyciele usług, a także administarcje łączności pochodzące ze wszystkich krajów Europy (obecnie ETSI liczy ok. 350 członków). Opłaty członkowskie zależą od ekonomicznych możliwości członków i są obliczane na podstawie rocznego obrotu, a w przypadku administracji — na podstawie produktu krajowego brutto w danym kraju.

## Slide 16
Notes: ETSI – siedziba we Francji

## Slide 17: ETSI Standard Preparation Procedure
Initiative to prepare a standard
Approval of the initiative by ETSI Technical Assembly
Preparation of the standard
Standard approval procedure
  Public evaluation of the draft
  Corrections
  Voting
Notes: Potrzeba opracowania nowego standardu europejskiego jest zgłaszana przez osobę, przedsiębiorstwo, bądź jedną z organizacji standaryzacyjnych, a następnie zatwierdzana przez Zgromadzenie Techniczne ETSI (ang. ETSI Technical Assembly). Od tej chwili staje się częścią programu prac ETSI.
Większość prac związanych z opracowywaniem standardu jest realizowanych przez jeden z Komitetów Technicznych ETSI, z których każdy zajmuje się odrębnym obszarem telekomunikacji. Komitet Techniczny określa zakres standardu, jego dokładny tytuł, a także wyznacza ekspertów odpowiedzialnych za wstępną wersję standardu. Eksperci ci spotykają się najczęściej w ramach Podkomitetu Technicznego, Grupy Ekspertów, bądź Grupy Projektu ETSI.
Po zatwierdzeniu wstępnej wersji standardu przez Komitet Techniczny, przesyła się go do Sekretariatu ETSI, który koordynuje proces jego zatwierdzania. Proces ten jest niezbędny, aby upewnić się, że standard może być zaakceptowany przez wszystkie zainteresowane strony. Procedura zatwierdzania trwa zwykle co najmniej 46 tygodni, ale w szczególnych przypadkach może być skrócona.
Po nie więcej niż czterech tygodniach od otrzymania wstępnej wersji standardu przez Sekretariat ETSI, następuje jego rozesłanie do 28 narodowych organizacji standaryzacyjnych w Europie w celu publicznej oceny. Organizacje te z kolei rozprowadzają wstępne wersje standardu między wszystkie zainteresowane instytucje w danych krajach (w tym również do instytucji nie będącymi członkami ETSI).
Narodowe organizacje standaryzacyjne mają zwykle 17 tygodni na przedstawienie swoich opinii i propozycji zmian. Ocena publiczna jest uznawana za ważną jeżeli swoje opinie prześle co najmniej połowa organizacji narodowych. Teraz z kolei ETSI musi w ciągu dwóch tygodni zebrać wszystkie opinie indywidualne i przesłać je do przewodniczącego odpowiedniego Komitetu Technicznego oraz z powrotem do narodowych organizacji standaryzacyjnych. W ciągu następnych ośmiu tygodni Komitet Techniczny rozważa ewentualne poprawki, a przez kolejne dwa tygodnie wprowadza się je do dokumentu.
Kolejnym etapem zatwierdzania standardu jest głosowanie. W ciągu ośmiu tygodni narodowe organizacje standaryzacyjne powinny zawiadomić ETSI o oficjalnym stanowisku swego kraju. Głosowanie jest ważne jeżeli co najmniej połowa organizacji narodowych weźmie w nim udział. Akceptacja standardu następuje gdy głosy pozytywne przekroczą 71% całkowitej liczby głosów. Jeżeli standard nie zostanie zaakceptowany, następuje ponowne głosowanie, tym razem wyłącznie wśród członków Unii Europejeskiej. Osiągnięcie co najmniej 71% głosów pozytywnych pozwala na przyjęcie standardu w państwach Unii Europejskiej.

## Slide 18: ITU-T and ETSI Standardization
Working document
Full standard
Technical report
Draft by Technical Committee
Nobody implements!
Technical report
Draft
of international standard
Still nobody implements!

## Slide 19: IETF Standardization
IETF: Internet Engineering Task Force
RFC: Request for Comments (Specification)
STD: Standard
RFCs outside the standardization track
  Experimental: denotes a specification that is part of some research or development effort
  Informational: informational documents from many sources
  Historic: obsolete document (purists have suggested that the word should be "Historical"; however, at this point the use of "Historic" is historical)
  Best Current Practice: best current practices for the Internet community

## Slide 20: IETF Standardization
At least two independent and inter-operational implementations
Historic document
Historic document
Significant implementation and operation experience
Internet Standard
RFC + STD
Internet Draft
I-D
Min 2 weeks
Max 6 months
RFC
IESG: Internet Engineering Steering Group
Proposed Standard
Min 6 months Max 24 months
IESG decision
Draft Standard
RFC
Min 4 months Max 24 months

## Slide 21: Examples of IETF Documents
RFC 1662 PPP in HDLC-like Framing. W. Simpson, Ed. July 1994. (Also STD0051) (Status: STANDARD)
RFC 3945 Generalized Multi-Protocol Label Switching (GMPLS) Architecture. E. Mannie, Ed. October 2004. (Status: PROPOSED STANDARD)
RFC 3912 WHOIS Protocol Specification. L. Daigle. September 2004. (Status: DRAFT STANDARD)
RFC 3936 Procedures for Modifying the Resource reSerVation Protocol (RSVP). K. Kompella, J. Lang. October 2004. (Also BCP0096) (Status: BEST CURRENT PRACTICE)
RFC 3976 Interworking SIP and Intelligent Network (IN) Applications. V. K. Gurbani, F. Haerens, V. Rastogi. January 2005. (Status: INFORMATIONAL)
RFC 4068 Fast Handovers for Mobile IPv6. R. Koodli, Ed. July 2005. (Status: EXPERIMENTAL)

## Slide 22: Example Next Generation Network:
ITU-T: A Next generation network (NGN) is a packet-based network which can provide services including telecommunication services and able to make use of multiple broadband, Quality of Service-enabled transport technologies and in which service-related functions are independent from underlying transport-related technologies. It offers unrestricted access by users to different service providers. It supports generalized mobility which will allow consistent and ubiquitous provision of services to users

## Slide 23: NGN: Problems to Solve
Regulatory framework related to network
Regulations facilitating introduction?
Regulations related to indoor cabling?
Regulations related to digging, aerial cables, cable conduit access?
Regulatory framework related to competition
Which type of competition is preferred by the regulator?
Is regulation necessary for the existence of the competition?
Implementation and provisioning
Does public support (financial and other) for introduction of NGN exist?
Are users migrating to NGN services?
Development of service ecosystem
Are services beyond triple-play possible?
Which providers are innovative?
Do infrastructure investors share service revenue?
Integration with economy
Are companies and public institutions migrating towards NGN?
Do health services, education, elderly care, etc. depend on NGA?
Telefonica, ITS Rome, 15.09.2008

## Slide 24: Challenge: Net Neutrality
savetheinternet.com: “Net Neutrality is the guiding principle that preserves the free and open Internet. Net Neutrality means that Internet service providers may not discriminate between different kinds of content and applications online”
Principles
  Freedom of access to services
  Freedom of access to content
  Freedom of access to devices
  Protection against abuses by operators
Net neutrality variations
  Strict net neutrality (no QoS guarantees whatsoever)
  Limited net neutrality (QoS allowed, but its differentiation cannot be based on user addresses but exclusively on traffic properties)

## Slide 25: No Net Neutrality
Rules:
  no regulations of any kind
  current Internet status
Who opts for it:
  telcos
  ISPs
Reasons:
  possibilities for extra charging content providers
  freedom in managing and developing the networks

## Slide 26: Strict Net Neutrality
Rules:
  no QoS allowed whatsoever
Who opts for it:
  non-technical parties
Reasons:
  QoS is not needed as, currently, Internet works sufficiently well

## Slide 27: Limited Net Neutrality
Rules:
  QoS is allowed, but the differentiation cannot be based on source or destination e.g.: we can prioritize all VoIP traffic, but not VoIP coming from a certain application or source/destination
Who opts for it:
  end-users
  content providers
Reasons:
  QoS is allowed but retains fairness
  traffic discrimination is prohibited

## Slide 28: Net Neutrality Seen by Involved Parties
Debate side | How do they see net neutrality? | Vote
Telecom operators | Unnecessary regulations (market rules are sufficient) | NO
Content providers | Fair competition, no double payments | YES
Technically aware users | Challenging, yet important step | ?
Technically unaware users | Freedom!!! | YES

## Slide 29: Net Neutrality Seen by Involved Parties
Debate side | How do they see the effects?
Telecom operators | The regulations will lessen the revenues, therefore, hindering the development of the networks
Content providers | The regulations will ensure fairness and promote development
Technically aware users | Regulations will promote fairness but may make network management more challenging
Technically unaware users | The regulations will enforce free and fair Internet

## Slide 30: Risks Associated with the Lack of Net Neutrality
“Better” Internet available only to a small fraction of the society
Higher charges for access to some www sites. Higher charges to companies owing these sites as well
Operators offering some services in their own networks can discriminate similar services offered by others
Limiting new service offerings (by limiting competition)

## Slide 31: Conclusion
Types of Telecommunication Companies
Regulation
Standardization in telecommunications
  ITU-T
  European standards organizations
  IETF vs. other standards organizations
Net Neutrality

## Slide 32: Thank you for your attention!