## Slide 1: Network and Service Management
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 12

## Slide 2: Outline
Introduction
Importance of management
Basic notions
Main functions of management systems
SNMP-based management
TMN-based management
Service management
Conclusion

## Slide 3: Definition of Network Management
Informally: Network management refers to the activities associated with running a network, along with the technology required to support those activities. A significant part of running a network is simply monitoring it to understand what is going on
Network management refers to the activities, methods, procedures, and tools that pertain to the operation, administration, maintenance, and provisioning of networked systems
Notes: A. Clemm, “Network Management Fundamentals”, Cisco Press, 2007

## Slide 4: OAMP
Operation deals with keeping the network up and running smoothly
Administration involves keeping track of resources in the network and how they are assigned
Maintenance is concerned with performing repair and upgrades
Provisioning is concerned with configuring resources in the network to support a given service
Notes: A. Clemm, “Network Management Fundamentals”, Cisco Press, 2007

## Slide 5: Importance of Network Management
Cost: the goal is to reduce and minimize the total cost of ownership (TCO) that is associated with the network
Quality of the communications and networking services that are provided
Revenue: network management can be a revenue enabler that opens up market opportunities
Notes: A. Clemm, “Network Management Fundamentals”, Cisco Press, 2007

## Slide 6: Examples
Failure of a large central office What revenue is lost when the central office of 50 000 subscriber lines is switched off (because of a software error) during 4 hours?
Costs of a cable cut The cable carries SDH STM-256 (40 Gbit/s). What revenue is lost under the assumption that the whole cable capacity is used by voice channels (64 kbit/s) and that the down time is 1 h?

## Slide 7: Scale of Network Management Systems
Some US operators say, that their manage-ment software contains 60 million lines of code. Assuming software productivity of 40 lines/day and 250 working days/year we get 6000 man-year of effort!
BT employs over 1000 management systems, over 10 hardware platforms (IBM, SUN, PC,...), over 15 programming languages (C, COBOL, SQL,...), over 15 operating systems (IBM MVS, UNIX, MS-DOS,...)
SPRINT (USA) says that management systems consume 50% of its total costs

## Slide 8: Management Automation Phases
Process automation requires system integration
Management systems can be integrated only if interface standards exist
Manual management
Partial automation
Process re-engineering
Automatic processes
Slow Ineffective Labor intensive Inflexible
Automation of some manual processes; manual management at interfaces between systems
Some processes
re-engineered to facilitate interoperation between systems
Fully automated processes; no manual
links; immediate service provision

## Slide 9: Management Functional Areas
Configuration management Creation, initialization, suspension, resumption, modification and deletion of managed objects; also reporting configuration changes
Performance management Evaluation and control of the performance of resources
Accounting management Monitoring of access to the resources and the collection and reporting of accounting information
Security management Support of the security policies
Fault management Detection and correction of faults or abnormal operations of resources
Notes: B. Hebravi, “GDMO: object Modelling & Definition for Network Management”, Technology Appraisals, 1995

## Slide 10: Example: Leased Line Management
Request for a leased line
    Search for available links (C)
    Allocation of links (C)
Monitoring of the used line (F, A, P)
If a failure is detected:
    Fault localization (F)
    Switching to a new route (C)
Billing (A)
Data ciphering if requested by a user (S)

## Slide 11: Management Layers
Element management
Network management
Service management
Business management

## Slide 12: Main Functions of Management Systems
Modeling and storing of management information
Transfer of management information
Processing of management information

## Slide 13: Representation of a Managed Object
Managed object
Real resource
Operations
Notifications
Object boundary

## Slide 14: Object-Oriented Design
Object
  Data + methods (functions)
  Objects communicate by sending messages
Object is an instance of its class
Class is a generic definition of objects characterized by common features

## Slide 15: Features of the Object-Oriented Approach
Encapsulation The internal operation of a managed object is not visible across the managed object boundary, unless management characteristics are defined to expose this information. All operations are performed by sending messages to the managed objects.
Inheritance and specialization Inheritance permits to define a managed object class by specializing an existing (more generic) managed object class. Specialization is obtained by defining additional packages that include new management attributes, operations, notifications or behaviors.
Notes: B. Hebravi, “GDMO: object Modelling & Definition for Network Management”, Technology Appraisals, 1995

## Slide 16: Features of the Object-Oriented Approach, cont.
Allomorphism Ability of a managed object belonging to some class to emulate another class
Containment A managed object can be regarded as contained within another managed object Applications:
  Hierarchical access and object control
  Hierarchical naming
Notes: B. Hebravi, “GDMO: object Modelling & Definition for Network Management”, Technology Appraisals, 1995

## Slide 17: Data Structures Used in Management
Inheritance tree Represents relations between managed object classes
Naming tree (containment or management information tree: MIT) Represents relation between object instances
Registration tree Used to identify definitions of classes, attributes, actions, notifications, and packets

## Slide 18: Inheritance Tree
Car
A: Number of wheels
Passenger car
A: Number of wheels, Speed
Race car
A: Number of wheels, Speed, Rotation rate
Truck
A: Number of wheels,
Carrying capacity
Dumper
A: Number of wheels,
Carrying capacity, Volume
Classes!

## Slide 19: Partial Inheritance Tree
connectivity
log
circuit
equipment
processingUnit
network
alarmRecord
logRecord
eventLogRecord
top

## Slide 20: Naming Tree
Car
No. 52343
Object instances!
Piston
No. 1
Engine
Piston
No. 2
Piston ring
Piston ring

## Slide 21: Partial Managed Object Naming Tree
root
network
equipment
software
circuit

## Slide 22: Partial Registration Tree
itu(0)
joint-iso-itu(2)
iso(1)
org(3)
dod(6)
internet(1)
directory(1)
mgmt(2)
experimental(3)
private(4)
MIB-1, MIB-II (1)
enterprises(1)
ROOT

## Slide 23: Manager-Agent Model
Manager
  In the managing system
Agent
  In the managed system (network element)
Managed objects (MIB: Management Information Base)
  Represent managed resources
  Created on the basis of the information model
Manger
Agent
MIB

## Slide 24: Management Models
Management by polling
  Manager sends management requests to agents
  Event detection related to the managed object is a sole responsibility of the manager
  Simple agent
Management by event notification
  Agent notifies the manager about events
  Event detection related to the managed object is a sole responsibility of the agent
  Complex agent

## Slide 25: Original SNMP Principles (Simple Network Management Protocol)
Temporary solution (TURNED TO BE LONG LASTING),
Management of IP equipment; the protocol dedicated to management of TCP/IP based networks
Simple protocol
First of all, fault and configuration management
CMIS/CMIP (Common Management Information Service / Common Management Information Protocol) previsioned as a long term solution

## Slide 26: Example: SNMP Managed Network
Management station
Agent
Host
Agent
Host
Agent
Terminal server
Agent
Device
Agent
Agent
Router
Data network
Device

## Slide 27: SNMP Operations
SNMP operation set is very limited
Reading of a parameter
Setting of a parameter
Sending an unconfirmed message (about occurrence of some events)
SNMP Operations: Get Request, Get-Next Request, Set-Request, Get-Response, Trap

## Slide 28: TMN (Telecommunications Management Network)
TMN
Telecommunications Network
Data Communication Network (DCN)
Node


Operations System
(OS)
Transmission System
Operations System
(OS)
Operations System
(OS)
Node
Node
Transmission System
TMN is a management network defined by standardized protocols, interfaces, and architecture

## Slide 29: TMN Architectures
Functional Architecture
  Elementary functions: Functional Components FC
  Several FC constitute a Functional Block FB
  Reference points between FBs
Physical Architecture
  Network resources divided into components
  Interfaces between components
Information Architecture
  Based on the manager-agent model
  Basic protocol: CMIP
  Notation: GDMO (Guidelines for the Definition of Managed Objects)

## Slide 30: TMN Physical Architecture
Components (building blocks)
  Operation Systems (OS)
  Mediation Devices (MD)
  Q Adapters (QA)
  Workstations (WS)
  Network Elements (NE)
  Data Communications Network (DCN)
Interfaces
  Q3
  Qx
  F
  X
DCN
DCN
DCN
OS
OS
OS
OS
OS
MD
DCN
DCN
DCN
NE
NE
NE
NE
NE
QA
NE
NE
NE
NE
NE
QA
NE
NE
WS
F
X/F/Q3
F/Q3
X
QX
QX
QX
Q3
Q3

## Slide 31: Service Management Tele-Management Forum Model
Objectives:
Establish an “industry-owned” common business model
Establish common process definitions to describe the functions of a service provider
Establish agreement on the information required to perform each process or function
Identify which processes are most in need of automation, and most dependent on industry agreement to support automation
Provide sufficient high-level information to serve as the starting point for detailed requirements development, and the satisfaction of those requirements through industry agreement

## Slide 32: Overview of Business Processes
Information Systems Management Processes
Service Planning/ Development
Service Configuration
Rating and Discounting
Service Quality Management
Service Problem Resolution
Service/Product Development and Maintenance Processes
Network Planning/ Development
Network/ Systems Administration
Usage/ Performance Data Collection
Network Monitoring/
Problem Resolution
Installation/ Maintenance
Network and Systems Management Process
Physical Network and Information Technology
Sales
Order Handling
Invoicing/ Collection
Performance Reporting
Problem Handling
Customer Care Processes
Customer Interface Management Process
Customer

## Slide 33: Sales Process
Business needs Sales inquiry
Available services/ features, prices, options
Capacity constraints
INPUTS
Customer
Customer
Interface Management
Service Planning/ Development
Service Quality Management
Sales Process
Orders, cancels
Forecasts
Service options
Customer
OUTPUTS
Status of inquiry
Special discounts
New service requirements
Order Handling
Customer
Interface Management
Service Planning/ Development
Service Quality Management
Learn about customer needs
Educate customer on services
Match expectations to offering
Arrange for appropriate options
Forecast service demand

## Slide 34: Current Issues in Management
Integration of management systems
TMN vs. SNMP
WWW-based management
Centralization vs. distribution of management
Self-management

## Slide 35: Conclusion
Importance of management
Basic notions
Main functions of management systems
SNMP-based management
TMN-based management
Service management

## Slide 36: Thank you for your attention!