## Slide 1: Basic Notions, Units, and Limits
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 2

## Slide 2: Outline
Signals
Decibels and related units
Transmission bandwidth
Bit rate and symbol rate
Claude Elwood Shannon
Laws of Moore, Sarnoff, and Metcalfe
Conclusion

## Slide 3: Signals
Signals are physical representations of messages
t
U
t
U
t
U
t
U
Discrete
Continuous
Discrete
Continuous
Value
Time

## Slide 4: Decibel [dB]
Power [dB] = 10 log (Pout/Pin)
Power ratio
dB
10
100
1 000
10 000
100 000
1/10
1/100
1/1000
10
20
30
40
50
– 10
– 20
– 30

## Slide 5: Decibel vs Bel
1 bel = 10 dB
1 bel: power ratio = 10
10 dB: power ratio = 10
1 dB: power ratio = 1,2589…
Rationale for using the logarithmic scale
  Log scale of the sensitivity of human senses
  Facilitates representation of very large and very small numbers
  Facilitates multiplications of ratios of physical entities (values expressed in dB are simply added)

## Slide 6: dBm
Power [dBm] = 10 log (power [mW] / 1 mW)
Example:
An amplifier has the output power of 20 W. Express the power in dBm.
Power [dBm] = 10 log (20 W / 1 mW) =
= 10 log (20  103 mW / 1 mW)  43 dBm

## Slide 7: dBW, dBmV
In microwave applications:
Power [dBW] = 10 log (power [W] / 1 W)
+ 30 dBm = 0 dBW
– 30 dBW = 0 dBm
In video transmission:
Voltage level
[dBmV] = 20 log (voltage [mV] / 1 mV) measured at the resistance of 75 

## Slide 8: Bandwidth
Definition (informal): The difference between the highest and the lowest frequency used for some purpose
Unit: hertz [Hz]

## Slide 9: Bandwidth (“3 dB”)
Frequency [Hz]
Attenuation [dB]
Why the 3 dB value was selected?
3 dB
Bandwidth

## Slide 10: Bit Rate and Signal Rate
Bit rate Amount of information transmitted in a unit time
Unit: bit/s
Signal rate Number of symbols transmitted in a unit time
Unit: baud (from the name Émile Baudot): one symbol per second

## Slide 11: Example: Quaternary Line Signal
10
01
10
01
11
00
10
10
01
10
1
2
3
0
Binary
Sequence
Two bits of digital information are represented by a four-level, or quaternary, line signal
Notes: Jednym z najczęściej używanych obecnie kodów transmisyjnych w styku U jest czterowartościowy kod 2B1Q. Pierwszym etapem kodowania 2B1Q jest podzielenie binarnego strumienia informacji na grupy dwubitowe. Wyodrębnianie grup rozpoczyna się od pierwszej pary bitów w ramce (nie licząc słowa synchronizacji ramki). Następnym etapem kodowania jest przypisanie każdej parze bitów jednego z czterech możliwych symboli (-3, -1, +1, +3). Pierwszy bit pary określa polaryzację symbolu (1 — dodatnia, 0 — ujemna), drugi natomiast jego amplitudę (1 — mała, 0 — duża). Oznaczeń symboli nie należy utożsamiać z przypisanymi im poziomami napięć. Jednakże stosunek poziomów napięć wysyłanych w łącze odpowiada stosunkowi oznaczeń liczbowych odpowiadających im symboli. Uzyskuje się w ten sposób jednakowy odstęp między każdym z poziomów równy 1/3 amplitudy międzyszczytowej.
Zastosowanie kodu czterowartościowego (związane z grupowaniem bitów strumienia informacyjnego w pary) obniża dwukrotnie prędkość transmisji w łączu.

## Slide 12: Bit Rate Versus Signal Rate
Example
V = 600 Bd, n = 2
K = 600 bit/s
V = 600 Bd, n = 4
K = 1200 bit/s
K bit rate in bit/s V signal rate in bauds
n the numbers of signal levels

## Slide 13: Bit Rate and Delay
Let’s compare a 10 Mb file transfer through two links of 10 000 km, of the bit rates of 1 kbit/s and 10 Gbit/s, respectively
What factor plays the most important role in the transmission time?
Let’s note that:
Transmission time of 1 bit through a link = transmission time over 1 km  link length (in km)
Time needed to input a message into a link = the number of bits in a message / bit rate

## Slide 14: Bits and Bytes
1 Byte [B] = 8 bits [bit, b]
1 Megabyte [MB] = … bits?
1 Mbit = 1 000 kbit = 1 000 000 bit
1 MB = 1 000 kB = 1 000 000 B
1 MiB = 220 B = 1 024 kiB = 1 048 576 B

## Slide 15: SI and Binary Prefixes
“The SI prefixes shall not be used to denote multiplication by powers of two.”
IEEE 1541-2002 Standard for Prefixes for Binary Multiples
September, 2009
SI prefix | Factor
kilo (k) | 103 = 1000
mega (M) | 106 = 1000 × 1000
giga (G) | 109
tera (T) | 1012
peta (P) | 1015
exa (E) | 1018
Binary prefix | Origin | Factor
kibi (Ki) | kilobinary | 210 = 1024
mebi (Mi) | megabinary | 220 = 1024 × 1024
gibi (Gi) | gigabinary | 230
tebi (Ti) | terabinary | 240
pebi (Pi) | petabinary | 250
exbi (Ei) | exabinary | 260

## Slide 16: Windows 7 – Disk Space
Used space:
22 304 935 936 B
22.3 GB
20.7 GiB

## Slide 17: SNR, BER
SNR: Signal-to-Noise Ratio
  Voice and TV channels require SNR > 50 dB
BER: Bit Error Rate The number of erroneous bits received divided by the total number of bits transmitted
  Example values: 10-6, 10-9, 10-12

## Slide 18: Claude Elwood Shannon 1916 – 2001
Born in 1916 in Michigan, USA
Universities:
  University of Michigan in Ann Arbor
  Massachusetts Institute of Technology (MIT): major: Electrotechnics and Mathematics
Master thesis He has shown that the Boole algebra can be applied to the design of logic devices (fundamentals of the automata theory) “the most influential Master thesis in the 20th century”

## Slide 19: Claude Elwood Shannon

## Slide 20: Claude E. Shannon: Ciphering
1940: Ph.D. in MIT
One year in the Institute for Advanced Study in Princeton, N.J.
1941 – 1956 Bell Laboratories Work on ciphering systems. Shannon has noticed that digital coding can protect information not only against unauthorized reading but also against other kinds of disturbance (e.g., noise)

## Slide 21: Claude E. Shannon: Information Theory
Shannon has shown that information can be measured
Amount of information is expressed by the probability of sending a given message by a source that can send a finite number of different messages
He has introduced a unit of information, i.e., a bit A bit is an amount of information carried in a message representing one of two equally probable states

## Slide 22: Amount of Information
If a source sends a sequence of symbols x1, x2,..., and each symbol xi appears with probability Pi , then this symbol carries the following amount of information:
Ii = –log2Pi = log2 (1/Pi )
If Pi is equal to 0.5, then Ii = 1 bit

## Slide 23: Example
Let’s assume that at an exam students were marked equal number of the following scores: “6”, “5”, “4”, “3”, “2”
What information (in bits) will receive a student who learns that his score was different than “2”?
How much more information does the student need to learn his score?
Hence: 2.32 – 0.32 = 2 bits are still needed

## Slide 24: Information Contents in a Single Binary Digit
The average amount of information reaches maximum (1 bit) for P = 0.5, i.e., when the two events are of
equal probability
H (average amount of information in a single binary digit, i.e., source entropy)
P (Probability of taking
of one of the two values)
0
0.5
1
1

## Slide 25: Claude E. Shannon: Channel Capacity Limit
C = W log2(1 + S/N)
C bit rate in bit/s (error free transmission)
W bandwidth in Hz
S/N Signal-to-Noise ratio
Example:
S/N = 1000 (30 dB)
W = 3100 Hz
C = ?

## Slide 26: Claude Elwood Shannon

## Slide 27: Claude E. Shannon: “Unified Field Theory of Juggling”
If
D is the dwell time, the time a hand spends holding an object
V is the vacant or empty hand time
F is the object's flight time
B stands for the number of objects tossed H stands for the number of hands doing the tossing
then B/H = (F + D)/(V + D)

## Slide 28: Moore’s Law
Gordon Moore (co-founder of Intel)
0
1995
200
400
600
800
1000
1200
2000
2005
2010
Processing power doubles
every 18 months
Source: CANARIE Inc.

## Slide 29: Sarnoff’s Law
David Sarnoff (broadcasting pioneer)
The total value of a broadcast communications network is proportional to the number of users
Justification: The value of, for example, a TV network is proportional to the number of viewers (similarly in the case of a newspaper)

## Slide 30: Metcalfe’s Law
Bob Metcalfe (Ethernet inventor)
The value of a communications network is proportional to the square of the size of the network
Justification: in a general communication network with n members, there are n (n – 1)/2 connections that can be made between pairs of participants. If all those connections are equally valuable, the total value of the network is proportional to n (n – 1)/2.
WRONG!

## Slide 31: Conclusion
Signals
Decibels and related units
Transmission bandwidth
Bit rate and symbol rate
Claude Elwood Shannon
Laws of Moore, Sarnoff, and Metcalfe

## Slide 32: Thank you very much for your attention