## Slide 1: Wireless Networking
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 10

## Slide 2: Outline
Introduction
Origins of mobile telephone systems
Cellular concept
Mobile cellular networks
UMTS
4G and 5G systems
WiFi and WiMAX
Conclusion

## Slide 3: First Mobile Telephone System
One and only one high power base station with which all users communicate
First mobile telephone system was developed and inaugurated in the U.S. in 1945 in St. Louis, MO
Entire Coverage Area
POTS
Wired connection
Notes: MO - Misouri

## Slide 4: Problems with Original Design
Original mobile telephone system could only support a handful of users at a time over an entire city!
With only one high power base station, users phones also needed to be able to transmit at high powers (to reliably transmit signals to the distant base station)
Car phones were, therefore, much more feasible than handheld phones, e.g., police car phones

## Slide 5: Cellular Concept
The cellular concept: multiple lower-power base stations that service mobile users within their coverage area and handoff users to neighboring base stations as users move
Together base stations tessellate the system coverage area

## Slide 6: Cellular Concept (2)
Thus, instead of one base station covering an entire city, the city was broken up into cells, or smaller coverage areas
Each of these smaller coverage areas had its own lower-power base station
User phones in one cell communicate with the base station in that cell

## Slide 7: Tessellation
Only three regular polygons tessellate:
  Equilateral triangle
  Square
  Regular Hexagon
Triangles
Squares
Hexagons
Notes: The summ of the angles must be equal to 360. Only triangle, square and hexagon perfectly divide 360.

## Slide 8: Circular Coverage Areas
Original cellular system was developed assuming base station antennas are omnidirectional, i.e., they transmit in all directions equally
Result: base station has circular coverage area
The most circular of the regular polygons that tessellate is the hexagon
Thus, researchers started using hexagons to represent the coverage area of a base station, i.e., a cell

## Slide 9: Evolution of Mobile Cellular Networks
1st generation, 1980s
  Analogue
  Voice
2nd generation 1990s
  Digital
  Voice, fax, data
3rd and 4th generation — now
  Digital
  Anywhere, anytime, anything
Most significant development in telecommunications in recent years
Notes: 2G – GSM
3G – UMTS
4G – LTE, WiMaX

## Slide 10: Cellular Structure and Frequency Spectrum Allocation Plan

## Slide 11: Common Cell Sizes
Pico cells
  Floor of a building
  A few meters
Micro cells
  Street
  10 – 400 meters
  Base station mounted below roof level
Macro cells
  5 km
  special masts erected for Base Station

## Slide 12: Important question
Would you like to have a Base Station in your vicinity?
Pros or cons:
  better signal strength
  more radiation

## Slide 13: Architecture of Cellular Networks
External
Network
Cellular Network
Mobile Station
Base Station
Mobile Switching Center
Server (e.g., Home Location Register)
Notes: 13

## Slide 14: Network Components: Mobile Station
Mobile Station
  Mobile Equipment (e.g., phone)
    Antenna
  Subscriber Identity Module (SIM)
    Smart card
    SIM must be inserted into ME before ME will work
    Essentially personalizes ME
    Contains subscription information
    Other information — subscriber’s short dialing codes

## Slide 15: Network Components: Base Station System
Base Transceiver Station
  Antenna
  Interfaces to MS
  Able to transmit /receive signals on many channels simultaneously
Base Station Controller
  Controls a number of Base Transceiver Stations
  Essentially a concentrator (multiplexer)
    Multiplexes BTSs onto a high speed link
  Undertakes some radio management tasks
    Passes Location Area Code to Base Transceiver Station for broadcasting to MSs
  Also translates 13 kbit/s speech from radio channels to 64 kbit/s PCM for transmission on fixed network

## Slide 16: Network Components: Mobile Switching Center (MSC)
ISDN switch enhanced to operate in a mobile network
In addition to switching
  Manages calls for all MSs within its domain
    Billing
    Handover
    Authentication

## Slide 17: Network Components: ‘Intelligence’ in Network
‘Intelligence’ essentially means databases
Equipment Identity Register (EIR)
  Stores information on lost or stolen MSs
  Each MS has a unique International Mobile Equipment Identifier (IMEI)
  Network can refuse access if IMEI is stored on EIR
Authentication Center (AuC)
  Provides access security for network

## Slide 18: Network Components: ‘Intelligence’ in Network, cont.
Home Location Register (HLR)
  One logical HLR in network
  Contains an entry for every subscriber
  Stores fairly static information about subscriber
    services subscribed to
  But also location information to allow mobility
    Location Area Code where MS is currently operating

## Slide 19: Network Components: ‘Intelligence’ in Network, cont.
Visitor Location Register (VLR)
  One VLR for every Location Area in network
  Typically a Mobile Switching Center ‘covers’ a location area
    In this instance VLR is integrated with MSC
  VLR contains information on every subscriber (visitor) currently operating in the domain of VLR
  Entries are added when visitors enter VLR domain
  Entries are deleted when visitors leave VLR domain
HLR and VLR jointly facilitate mobility

## Slide 20: GSM Network Architecture
NMC/
OMC
MSC
EIR
VLR
HLR
AUC
GMSC
D
C
E
To PSTN/ISDN
A
F
B
MS
MS
MS
MS
MS
BTS
BTS
BTS
BTS
BTS
U
m
BSC
BSC
A
bis

## Slide 21: GSM
TDMA/FDMA
Used frequency bands: 900/1800/1900 (400) MHz
Carrier spacing: 200 kHz
D-AMPS (IS-54, IS-136)
TDMA/FDMA
Used frequency bands : 800/1900 MHz
Carrier spacing: 30 kHz
PDC
TDMA/FDMA
Used frequency bands : 700/1500 MHz
Carrier spacing: 25 kHz
Mobile Radio Networks
Notes: D-AMPS (Digital-Advanced Mobile Phone Service) – druga generacja cyfrowej technologii transmisji TDMA. TDMA operowało w Ameryce Północnej w pasmach PCS 800 MHz i 1.9 GHz. Znane także pod nazwą IS-136 oraz IS-54.
PDC (Personal Digital Cellular) - jest systemem telefonii komórkowej drugiej generacji wynalezionym i używanym w Japonii.

## Slide 22: GSM, Phase 2+
HSCSD (High-Speed Circuit-Switched Data) 4  14.4 kbit/s = 57.6 kbit/s (better channel coding)
GPRS (General Packet Radio Service) 8 slots  14.4 kbit/s = 115.2 kbit/s (slot sharing, packet interleaving)
CAMEL (Customized Application for Mobile Enhanced Logic)
ASCI (Advanced Speech Call Items)

## Slide 23: 3G Systems
Offered Services:
Efficient e-mail service
www browsing
Corporate LAN access
Videoconferencing
E-commerce
Multimedia
UMTS: Unlimited Money To Spend
Higher bandwidth due to WCDMA
Technical implementation:

## Slide 24: WCDMA (Europe)
Wideband CDMA
Bit rates up to 2 Mbit/s
Duplexing
  FDD (symmetrical streams)
  TDD (asymmetrical streams)
Required bandwidth: 5 MHz (cdmaOne: 1.25 MHz)
Coherent reception (upstream)
Power control in a closed loop (downstream)
Multipath link (downstream)
Asynchronous and synchronous cell search procedure
Soft and hard handover
Notes: Hard Handover: Hard handover means that all the old radio links in the UE are removed before the new radio links are established. Hard handover can be seamless or non-seamless. Seamless hard handover means that the handover is not perceptible to the user. In practice a handover that requires a change of the carrier frequency (inter-frequency handover) is always performed as hard handover. Soft Handover: Soft handover means that the radio links are added and removed in a way that the UE always keeps at least one radio link to the UTRAN. Soft handover is performed by means of macro diversity, which refers to the condition that several radio links are active at the same time. Normally soft handover can be used when cells operated on the same frequency are changed.

## Slide 25: 3G Networks
Large Coverage
Outdoor - High Mobility
Up to 14Mbps
Notes: Currently we are using 3G systems
This system provides large coverage with high mobility to the user
This system can support up to 14Mbps to the user
Currently this would be able to provide low quality video streams and web browsing along with the
the basic mobile functions to all users

## Slide 26: 4G Networks
High coverage – 100 Mbit/s
High mobility outside buildings
Macrocells
Picocells
Isolated “hotspots” – 1 Gbit/s
Very low mobility indoors
Notes: Future Wireless like 4G invision lots more bandwidth for the growing public
There will be not only high mobility with good data rates but also super high data rates in hotspot environments
Not only do they envision the support for 4G rates but also they expect the phones to support previous wireless standards too
These will all be accessible by one device which needs to be flexible and change rapidly between these types of coverage
Now let’s take a look at what comprises the 4G wireless system

## Slide 27: 4G Networks (2)
Higher bit rates and higher reliability than in 3G
100 Mbit/s
Lower cost than in 3G
System uses a variety of standards
Bluetooth, wired and wireless systems
Ad hoc networks
IPv6 in the core network
Use of OFDM instead of CDMA

## Slide 28: Evolution Towards 5G
1G
Internet
2G/2.5G
Internet
Digitalization
Packet networks
3G/4G
Internet
Manufacturer
Internet
Internet of Vehicles
Smart Grid
Internet of Things
5G
Źródło: T. Russell Hsing
Manufacturer
Manufacturer

## Slide 29: 5G Transformative Benefits and Uses
5G will provide massive capacity, speed, and latency improvements. 5G networks will:
  Support 100 times more traffic than 4G
  Increase peak speeds from 4G by a factor of 20
  Decrease latency from 4G by a factor of 10
5G is anticipated to enable innovation in industries across the economy, including:
  self-driving cars
  logistics
  Internet of Things
  smart grid electric systems
  public safety
  health and wellness
  and smart cities

## Slide 30: Requirements and Technologies
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr | 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
5G Networks
Increased data rate & network capacity
Densification, FDD, CRN, mMIMO, D2D communication, full duplex radio
Ubiquitous connectivity
Multi-RAT, self-heal, densification, CRN, NFV, SDN, C-RAN, RANaaS, CONCERT,
Low latency
Cache, fast handoff, D2D communication, mobile small-cells, self-heal
Scalability
QoS
Security & privacy
Interference & handoff management
NFV, SDN, C-RAN, RANaaS, CONCERT
Delay-bound QoS, Quality management equipment, multi-links with multi-flow and multi-QoS
C-RAN, VLC, mmWave, mMIMO, small-cells, D2D communication, user separation
Monitoring and
encryption-decryption
SIC, CRN, advance receiver, joint detection/decoding
Inter-tier, intra-tier, and
multi-RAT handoff,
Environmental friendly & less money

## Slide 31: IEEE 802.11 (WiFi)
WiFi: Wireless Fidelity
Wireless local area network (WLAN)
Coverage of an area of app. 100 m diameter
Simplicity of the solution
Unlicensed band: 2.4–2.5 GHz and 5 GHz
Maximum bit rate: up to 600 Mbit/s

## Slide 32: IEEE 802.11 Standardization
802.11 (1997)
  Bit rate: up to 2 Mbit/s; band: 2.4-2.5 GHz
802.11a (1999)
  Bit rate: up to 54 Mbit/s; band: 5.0 GHz
802.11b (1999)
  Bit rate: up to 11 Mbit/s; band: 2.4-2.5 GHz
802.11g (2003)
  Bit rate: up to 54 Mbit/s; band: 2.4-2.5 GHz
802.11n (2009)
  Bit rate: up to 600 Mbit/s; band: 2.4 or 5.0 GHz
Notes: 802.11 defines the PHY (physical) and MAC (media access control) layers of the protocol. All other layers are identical to IEEE 802.3 (the Ethernet).
The IR (infrared) physical layer is essentially an orphan.
802.11a was proposed before 802.11b, hence the ‘a’ designation. However, 802.11b came to market first. As of Mid 2001, a few companies have 802.11a radios available in sample quantities. There are not 802.11a WLAN systems available.

## Slide 33: IEEE 802.16 (WiMAX)
WiMAX: Worldwide Interoperability for Microwave Access
Achieved bit rates: 10 Mbit/s (theoretically up to 100 Mbit/s)
Reach: up to 20 km (up to 10 km for indoor terminals)
Transmission technology: OFDM (Orthogonal Frequency Division Multiplexing)

## Slide 34: IEEE 802.16 Standardization
IEEE 802.16 (2001)
  Band 10 – 66 GHz
  Line Of Sight required (LOS); 2 – 5 km
IEEE 802.16a (2003)
  Band 2 – 11 GHz (Currently: 2.5, 3.5, 5.7 GHz)
  NLOS
IEEE 802.16-2004 (2004)
  Consolidated version of previous standards
  Reach: 5 – 50 km
IEEE 802.16e (2005)
  Extension of IEEE 802.16-2004
  Limited mobility (up to 60 km/h)

## Slide 35: IEEE 802.16m
New radio interface
Bit rates 100 Mbit/s for mobile devices 1 Gbit/s for fixed users
Cellular network structure
Bandwidth: 20 MHz or more
Standard approved: March 2011

## Slide 36: Comparison of WiFi and WiMAX
 | WiFi (802.11) | WiMAX (802.16)
Bit rate | 54 Mbit/s/channel 20 MHz | 26.2 Mbit/s/channel 7 MHz
QoS | No guaranties (except 802.11e) | Five QoS classes
Reach | App. 100 m | Up to 20 km (up to 10 km for indoor)
Frequency bands | Unlicensed | Unlicensed or licensed
Typical use | WLAN | Fixed wireless access, limited mobility

## Slide 37: IEEE 802.20 (MBWA, MobileFi)
MBWA: Mobile Broadband Wireless Access
Mobility: up to 250 km/h
Band: below 3.5 GHz (licensed)
Bandwidth: 1.25 MHz or 5 MHz
Bit rates
  Downlink: up to 4 Mbit/s (5 MHz)
  Uplink: up to 1.2 Mbit/s (5 MHz)
Standard approved in 2008
Put to hibernation on March 2011 due to lack of activity

## Slide 38: Conclusion
Origins of mobile telephone systems
Cellular concept
Mobile cellular networks
UMTS
4G and 5G systems
WiFi and WiMAX

## Slide 39: Thank you very much for your attention