## Slide 1: Key Networking Issues
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 7

## Slide 2: Outline
Introduction
Hierarchy in telecommunications networks
Network types
Switching methods
Access technologies
Cloud computing
Conclusion

## Slide 3: Examples of Telecommunications Networks
The number of links for n end nodes:
n (n – 1)/2
The number of links for n end nodes:
n

## Slide 4: Hierarchical Telecommunications Network

## Slide 5: Hierarchical Telecommunications Network
5
Int.
Office
Toll
Offices
Area 3
Area 1
Area 2
Area 4

## Slide 6: Example of Information Network
Transit network 1
Transit network n
Local network n
Local network 1
Backbone network n
Backbone network 1
Access network
Access network
LO
LO: Local Office (or Service Node)
TO: Transit Office
LO
TO
TO
TO
TO

## Slide 7: Network Tiers
A tier 1 network is an IP network that participates in the Internet solely via settlement-free interconnection, also known as settlement-free peering
A tier 2 network is an IP network that engages in the practice of peering with other networks, but still purchases IP transit to reach some portion of the Internet
A tier 3 is sometimes also used to describe networks who solely purchase IP transit from other networks (typically tier 2 networks) to reach the Internet

## Slide 8: Tier 1 Networks
Name | Headquarters | AS number | Degree
AT&T | USA | 7018 | 2365
Centurylink | USA | 209 / 3561 | 1367
Deutsche Telekom AG | Germany | 3320 | 535
Inteliquent (formerly Tinet) | USA | 3257 | 886
Verizon Business (formerly UUNET) | USA | 701 | 1946
Sprint | USA | 1239 | 1183
TeliaSonera International Carrier | Sweden | 1299 | 630
NTT Communications | Japan | 2914 | 718
Level 3 Communications | USA | 1 / 3356 / 3549 | 4402
Tata Communications | India | 6453 | 569
Internet traffic is relying less on U.S. networks than previously
Notes: degree - Number of ASes with direct peering or customer-provider links to the neighbor AS.
A 2008 report shows Internet traffic relying less on U.S. networks than previously.

## Slide 9: Tier 2 Networks (Examples)
Atrato IP Networks AS5580 (buys transit from Deutsche Telekom AG/AS3320 and GBLX)
Vodafone AS3209 (formerly ARCOR AG Germany) (buys transit from Level3/AS3356, GBLX/AS3549)
Virgin Media/ Virgin Media Business
France Télécom AS5511 (buys transit from Verizon/AS701, possible paid peering from Sprint/AS1239)
Tele2 (formerly SWIPNet) AS1257 (buys transit from Sprint/AS1239)
Comcast AS7922 (buys transit from Tata Communications/AS6453)

## Slide 10: Switching Methods
Circuit switching
Message switching
Packet switching

## Slide 11: Circuit Switching
Network nodes
SubB
SubA

## Slide 12: Message Switching
Message
Message
Message
Message
Nodes with memory
SubB
SubA
Notes: Komutacja wiadomości polega na przesyłaniu między stacjami końcowymi informacji w postaci wiadomości zawierających adres stacji docelowej, przy czym wiadomości te mogą być przechowywane przez pewien czas, jeżeli jest to niezbędne, w węzłach sieci, zanim zostaną przesłane dalej. W tej metodzie komutacji kanały są zajmowane tylko w czasie rzeczywistego przesyłania wiadomości między sąsiednimi węzłami. Zwiększa to, w porównaniu z komutacją łączy, efektywność wykorzystania sieci telekomunikacyjnej, kosztem wprowadzenia większych i nierównomiernych opoźnień. Komutacja wiadomości jest stosowana w sieci telegramowej.

## Slide 13: Packet Switching
Message partition into packets

## Slide 14: Packet Switching
Packet 2
Packet 2
Packet 1
Packet 1
Nodes with memory
Packet 1
Packet 2
SubB
SubA

## Slide 15: Origins of Packet Switching: Paul Baran (1926–2011)
A
B
Born in Grodno, Poland

## Slide 16: Access Technologies
Evolution of access networks
xDSL technologies
Optical access networks
MAN example: Resilient Packet Ring

## Slide 17: Access First Mile Solution
Small/Medium Business
Fiber, Copper
Broadband
Wireless
Wireless data/video
Mobile Computing
Enterprise/ Business
Broadband
Fiber
Copper, Fiber, Coax
Residential and Telecommuting
Notes: Np. Ethernet w całej sieci – a nie tak jak teraz że jest sieć PSTN i w last mile jest inna technika, np. ADSL.
Ethernet in the first mile (EFM) refers to using one of the Ethernet family of computer network protocols between a telecommunications company and a customer's premise.
From the customer's point of view it is their "first" mile, although from the access networks' point of view it is known as the "last mile"

## Slide 18: Evolution of Access Networks
Analog telephone line
ADSL
FTTx, VDSL2,
ADSL2plus
ISDN
Improved copper
Fiber/ copper
Fiber
FTTH
Source: DSL Forum

## Slide 19: ADSL Connection
ADSL Modem
POTS
Filter
Mbit/s
kbit/s
ADSL Modem
POTS
Filter
POTS
Line card
Mbit/s
kbit/s
Line
Exchange termination
User termination

## Slide 20: ADSL Spectrum
Power
Frequency
Voice
Upstream
Downstream
Neostrada bitrates in Mbit/s:
2012: 2015:
* 2/0.25 * 10/1
* 6/0.5 * 20/1
* 10/1 * 80/8
* 20/1

## Slide 21: xDSL Technologies
Type | ITU | Maximum bit rates | Year
ADSL (Asymmetric DSL) | G.992.1 | 7 Mbit/s downstream 800 kbit/s upstream | 1999
ADSL2 | G.992.3 | 8 Mbit/s downstream 1 Mbit/s upstream | 2002
ADSL2plus | G.992.5 | 24 Mbit/s downstream 1 Mbit/s upstream | 2003
ADSL2-RE | G.992.3 | 8 Mbit/s downstream 1 Mbit/s upstream | 2003
SHDSL (Symmetric High-speed DSL) | G.991.2 | 5.6 Mbit/s symmetric | 2003
VDSL (Very high-speed DSL) | G.993.1 | 55 Mbit/s downstream 15 Mbit/s upstream | 2004
VDSL2 - 12 MHz long reach | G.993.2 | 55 Mbit/s downstream 30 Mbit/s upstream | 2005
VDSL2 - 30 MHz short reach | G.993.2 | 100 Mbit/s symmetric | 2005

## Slide 22: xDSL Technologies, cont.
Short links only
VDSL
Too low bit rates for 3 HDTV channels
ADSL2+
VDSL2 = Bit rate of VDSL with the ADSL/2+ reach
SHDSL
Too low bit rates for Triple Play
Bit rate
[Mbit/s]
2
8
100
20
60
Link length
1 km
2 km
3 km
4 km
5 km

## Slide 23: Fiber-based Access Networks
Fiber to the User implemented with the PON or Ethernet technologies
  Fiber to the Home (FTTH)
  Fiber to the Building (FTTB)
Fiber to the User implemented with the PON technology
  Fiber to the Premises (FTTP)
Fiber covering a part of the distance
  Fiber to the Neighborhood (FTTN)
  Fiber to the Node (also FTTN)
  Fiber to the Curb (FTTC or FTTK: kerb)
  Fiber to the Cabinet (also FTTC)

## Slide 24: Passive Optical Networks
//
//
//
//
//
//
//
//
ONU
OLT
Optical splitter typically: 1  16 lub 1  32
In most cases: 10-20 km
Source: FTTH Council
  ONU: Optical Network Unit
  OLT: Optical Line Termination

## Slide 25: Passive Optical Networks (2)
//
//
//
//
//
//
//
//
1550 nm (optional video)
1490* nm (data)
1310 nm (data)
* Data can be sent at 1550 nm if this wavelength is not used for video transmission
ONU
OLT
Source: FTTH Council

## Slide 26: Resilient Packet Ring (RPR)
IEEE 802.17 RPR is a new technology for ring-based metropolitan area networks that enables an efficient transfer of data traffic as well as fast protection mechanisms
It is a protocol that consists of a superset of features derived from various proprietary solutions such as Cisco Systems’ DPT (Dynamic Packet Transport) and Nortel Networks’ Optera

## Slide 27: Advantages of RPR
Advanced protection mechanisms
Distributed control
Interoperability with major transmission standards
Scalability in speed and number of nodes
Plug-and-play operation
Performance monitoring capabilities
Support for a limited number of priorities
OAM and advanced traffic and bandwidth management
Support for unicast, multicast and broadcast data traffic

## Slide 28: RPR Ring
Node 0
Node 7
Node 6
Node 5
Node 4
Node 3
Node 2
Node 1
Data packets
Control packets
Inner ring
Outer ring

## Slide 29: Node and Ring Structures in RPR
PTQ: Primary Transit Queue (class A)
STQ: Secondary Transit Queue (class B/C)
A
B
C
Control frames
Shaper
}
{
PTQ
STQ
Check
Client
Adjust
Control data path
Transit in
Transit out
Filter
Transit queues
Notes: Check: against bit errors and time-to-live expiration
Filter: decides whether the frame should be copied to the client, passed to the control sublayer, or neither
Adjust: stripping frames from the ring, djusting frame fields (e.g., the time-to-live field) and placing the frame in the correct tranit queues

## Slide 30: RPR: Traffic Classes
Traffic class |  |  | Quality of Service |  |  | 
Name | Example applications | Sub-class | Guaranteed bandwidth | Delay/ jitter | Bandwidth type | Bandwidth subtype
Class A | Real-time applications | Subclass A0 | Yes | Low | Allocated | Reserved
 |  | Subclass A1 |  |  |  | On demand
Class B | Real-time applications with low delay | Class B-CIR | Yes | Limited | Allocated | 
 |  | Class B-EIR | No | Un-limited | Allocated if possible | 
Class C | Best effort | — |  |  |  | 
CIR: Committed Information Rate
EIR: Excess Information Rate
Notes: CIR: Committed Information Rate
EIR: Excess Information Rate

## Slide 31: Intelligent Protection Switching (IPS)
Automatic reaction protocol in case of node or link failure
Information about failures:
  from the physical layer (Loss of Signal),
  missing continuity of signal transport in the RPR layer (continuity check)
Two mechanisms:
  steering
  wrapping
Assumption on breaks in transmission: no longer than 50 ms

## Slide 32: A Five-Node RPR Ring
1
3
5
4
2
Fibre cut

## Slide 33: Fairness Algorithm
Fair access to the bandwidth for low and medium traffic (C and B classes, respectively)
  Global Fairness – assumption on no congestion in network
  Local Optimization – each node can locally use more bandwidth (more than is calculated by fair division) till another node does not want to transmit more data
Two algorithm versions:
  equal-weighted fairness – prevents to take advantage by nodes entering traffic to the ring
  unequal-weighted fairness – access to the bandwidth is dependent on node weights

## Slide 34: Topology Discovery
Protocol enables topology change (plug & play)
Enables fast recognition of RPR ring configuration change
Related to the protection protocol – common control mechanisms, access to the common databases
Automatic recognition of configuration
Initiated in time of the beginning of ring operation and in time of any topology modification
Periodically sending control frames (TD frames)

## Slide 35: Cloud Computing
Cloud Computing is a general term used to describe a new class of network based computing that takes place over the Internet,
  a collection/group of integrated and networked hardware, software and Internet infrastructure (called a platform)
  Using the Internet for communication and transport provides hardware, software and networking services to clients
These platforms hide the complexity and details of the underlying infrastructure from users and applications by providing very simple graphical interface or API (Applications Programming Interface)

## Slide 36: Cloud Computing (2)
In addition, the platform provides on demand services, that are always on, anywhere, anytime and any place
Pay for use and as needed, elastic
  scale up and down in capacity and functionalities
The hardware and software services are available to
  general public, enterprises, corporations and businesses markets

## Slide 37: Cloud Data Characteristics
Remotely hosted: Services or data are hosted on remote infrastructure
Ubiquitous: Services or data are available from anywhere
Commodified: The result is a utility computing model similar to traditional that of traditional utilities, like gas and electricity — you pay for what you would want!

## Slide 38: Cloud Service Models
Software as a Service (SaaS)
  Use provider’s applications over a network
  User does not manage or control the network, servers, OS, storage or applications
Platform as a Service (PaaS)
  Users deploy their applications on a cloud
  Users control their applications
  Users do not manage servers, OS, storage
Notes: Cloud Software as a Service (SaaS). The capability provided to the consumer is to use the provider’s applications running on a cloud infrastructure and accessible from various client devices through a thin client interface such as a Web browser (e.g., web-based email). The consumer does not manage or control the underlying cloud infrastructure, network, servers, operating systems, storage, or even individual application capabilities, with the possible exception of limited user-specific application configuration settings.
Cloud Platform as a Service (PaaS). The capability provided to the consumer is to deploy onto the cloud infrastructure consumer-created applications using programming languages and tools supported by the provider (e.g., java, python, .Net). The consumer does not manage or control the underlying cloud infrastructure, network, servers, operating systems, or storage, but the consumer has control over the deployed applications and possibly application hosting environment configurations.
Cloud Infrastructure as a Service (IaaS). The capability provided to the consumer is to provision processing, storage, networks, and other fundamental computing resources where the consumer is able to deploy and run arbitrary software, which can include operating systems and applications. The consumer does not manage or control the underlying cloud infrastructure but has control over operating systems, storage, deployed applications, and possibly select networking components (e.g., firewalls, load balancers).

## Slide 39: Cloud Service Models (2)
Infrastructure as a Service (IaaS)
  Rent processing, storage, network capacity, and other fundamental computing resources
  Consumers gets access to the infrastructure to deploy their stuff
  Do not manage or control the infrastructure
  Do manage or control the OS, storage, applications, selected network components
To be considered “cloud” they must be deployed on top of cloud infrastructure that has the key characteristics

## Slide 40: Cloud Service Models (3)

## Slide 41: General Trend
Wireless networks will become fixed
networks, and fixed networks will
become wireless networks

## Slide 42: Past
Radio link
Copper
lines
Copper
lines

## Slide 43: Present
Radio
links
Radio
links
Optical fiber

## Slide 44: Conclusion
Hierarchy in telecommunications networks
Network types
Switching methods
Access technologies
Cloud computing

## Slide 45: Thank you very much for your attention