## Slide 1: Signal Coding
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 6

## Slide 2: Outline
Introduction
Source coding
Error detecting and error correcting coding
Channel coding
Line coding
Coding for security
Conclusion

## Slide 3: Binary Codes
Examples
ASCII (American Standard Code for Information Interchange)
EBCDIC (Extended Binary Coded Decimal Interchange Code)
Character ASCII EBCDIC
a 1100001 10000001
b 1100010 10000010
1 0110001 11110001
2 0110010 11110010
SYN 0010110 00110010
ETX 0000011 00000011

## Slide 4: Morse Code
A  —
B —   
C —  — 
D —  
E 
Morse code was invented by ...
Alfred Vail
Notes: ”Veil invented the telegraph key and the efficient Morse code...
Morse continued to insist on the use of his dictionary approach in which digits were assigned to specific words along with a paper record of the received message, but Vail felt that approach was far too cumbersome. Accordingly, Vail went to a local newspaper and counted the quantity of each letter used to set type. Based on the frequency of occurrence, Vail then devised the efficient dot-dash scheme known today as Morse code.”
A. Michael Noll, Principles of Modern Communications Technology, Artech House, Boston, 2001

## Slide 5: David A. Huffman (1925 – 1999)
In 1952, as an MIT student, in his term project, he proposed a new coding scheme (the task was to find the most efficient binary representation of symbols)
He worked on the project over several months

## Slide 6: Huffman Coding (2)
Basic idea:
  assign a shorter code to those characters that occur more frequently
Would this work?
How would you decode the 01 sequence?
Symbol | Frequency | Code
A | 10 | 0
B | 7 | 1
C | 5 | 00
D | 3 | 01

## Slide 7: Huffman Coding
No code is the prefix of another code
Decode: 100110 – no ambiguity here
Symbol | Frequency | Bad Code | Good Code
A | 10 | 0 | 0
B | 7 | 1 | 10
C | 5 | 00 | 110
D | 3 | 01 | 111

## Slide 8: How to Construct a Huffman Code?
Example
Six letters of given probabilities of occurrence have to be sent
xi P (xi)
A, B 0.3
C 0.13
D,E,F 0.09
Construct a Huffman code

## Slide 9: Huffman Codes
A 0.30
B 0.30
C 0.13
D 0.09
E 0.09
F 0.09
0.6
0.22
0.18
1
0
1
0
1
0
0.4
1
0
1
1
0
11
10
011
010
001
000

## Slide 10: Image Coding Standards
ISO JPEG (Joint Photographic Experts Group)
ISO MPEG (Moving Picture Experts Group)
  MPEG-1: standard for storing multimedia information on CD-ROMs (1.5 Mbit/s)
  MPEG-2: standard for broadcasting television (1.5 – 20 Mbit/s)
  MPEG-3: standard for HDTV (replaced by MPEG-2)
  MPEG-4: standard for mobile communications (1999)
  MPEG-7: standard for content description (2000)
  MPEG-21: standard for identification and content protection of multimedia

## Slide 11: MPEG-1: ISO and IEC Standards
IS 11172-1: System Synchronization and multiplexing of visual and acoustic signals
IS 11172-2: Video Compression of no interleaved video signals
IS 11172-3: Audio Compression of acoustic signals
IS 11172-4: Conformance Tests Procedures for testing of coding and decoding processes

## Slide 12: MPEG-1; IS 11172-3
Three coding systems for acoustic signals
  Layer-1: recommended 192 kbit/s
  Layer-2: recommended 128 kbit/s
  Layer-3: recommended 64 kbit/s
In each layer a data stream format and decoder are defined (coder is not standardized)
MP3: An MPEG 1 Layer-3 algorithm Data compression achieved: 12 : 1 (comparing to CD)

## Slide 13: Other Sound Coding Techniques
Mp3Pro
  Standard set by a Swedish company Coding Technologies, and licensed by Thomson Multimedia
  Allows for decreasing sound files even by 50% comparing to MP3
MP4
  Based on MPEG-4 and the AAC (Advanced Audio Coding) standard, but is a proprietary solution (Global Music One)

## Slide 14: Error Detecting and Error Correcting Coding
Error detecting coding
  Parity control
  Cyclic Redundancy Check (CRC)
Error correcting coding
  Repetition coding
  Other error correcting approaches

## Slide 15: Parity Control
0 0 1 1
1 0 0 0
1 1 1 0
0 1 1 0
0
1
1
0
Parity bit
Binary sequence
0 1 1 1
1 0 0 0
1 1 1 0
0 1 1 0
0
1
1
0
Parity bit
Binary sequence
Error!

## Slide 16: CRC: Checksum Generation
Sender:
1. Select generating polynomial G(x) of order r
2. Append r zeroes to the original sequence of length k
3. Divide (modulo 2) the original sequence by the sequence representing G(x)
4. Append the resulting reminder to the original sequence; send the received sequence

## Slide 17: CRC: Sender Example
Generating polynomial: G(x) = x 2 + 1
It is represented by the binary number: 101
11001 : 101
101
110
101
111
101
10
Data bits
Divisor
CRC
Bits to send: 1100110

## Slide 18: CRC: Checksum Generation
Receiver:
1. Divide (modulo 2) the received sequence by the sequence representing G(x); a transmission error appeared if the reminder is not equal to zero

## Slide 19: CRC: Receiver Example
1100110 : 101
101
110
101
111
101
101
Received bits
Divisor
101
000
No error

## Slide 20: Effectiveness of 16-bit Long Checksum
ITU-T V.41: G(x) = x16 + x12 + x5 + 1
In case of data blocks of up to 3860 bits the system will detect:
All odd numbers of errors within a block
All double errors
Any error burst not exceeding 16 bits in length
A large percentage of other error patterns
Probability that an error is not detected:  10–14

## Slide 21: Error Correcting Coding Repetition Code
5 errors in the channel resulted in only a single error in the outgoing stream!
Digital source signal 1 0 1 1
Coder output 111 000 111 111
Channel output 110 110 011 101
Decoder output 1 1 1 1

## Slide 22: Error Correcting Coding Example of a Simple Coding System
Replacing “1” by “0” at the intersection of the row and the column at which an error appeared will correct it
0 0 1 1
1 0 0 0
1 1 1 0
0 1 1 0
0
1
1
0
Parity bit
Binary sequence
0 0 1 1
Error!
Error!
Parity bits for columns
0 0 1 1
0 1 1 1
1 0 0 0
1 1 1 0
0 1 1 0
0
1
1
0
Parity bit
Binary sequence

## Slide 23: Forward Error Control (Channel Coding)
FEC: Forward Error Control
The aim of FEC is to lower the effective bit error rate in a channel by adding some redundancy to the information sent by this channel
Two types of channel coding
  Block codes: operate on blocks of data (several hundreds of bytes)
  Convolutional codes: operate on serial data (a few bits are processed at a given instant)

## Slide 24: Example of a Block Code Reed-Solomon Codes
A Reed-Solomon code is specified as RS (n,k) with m-bit symbols,
where:
  k is the number of data symbols being encoded,
  n is the total number of code symbols in the encoded block
  m is the number of bits in one symbol
Applications: CDs, DVDs, Blu-ray Discs, QR Codes, DSL, WiMAX, broadcast systems such as DVB and ATSC, storage systems such as RAID 6, satellite communications

## Slide 25: Reed-Solomon Codes (2)
The code is capable of correcting any combination of t or fewer errors:
The code is capable of detecting any combination of 2t or fewer errors:

## Slide 26: Reed-Solomon Codes (3)
A popular Reed-Solomon code is RS (255,223) with 8-bit symbols. Each code word contains 255 code word bytes, of which 223 bytes are data and 32 bytes are parity.
For this code:
  n = 255, k = 223, m = 8
  2t = n – k = 32, t = 16
The decoder can:
  correct any 16 symbol errors in the code word
  detect any 32 symbol errors in the code word

## Slide 27: Andrzej Głowacki. Archetypture: Aesthetics of QR Codes
Exhibition at the Manggha Museum, Krakow
Oct. 29, 2015 —
Feb. 21, 2016

## Slide 29: Example of a Convolutional Coder (1/2)
In a convolutional code each block of k bits is mapped to a block of n bits, where the n bits are defined not only by the k current information bits, but also by some earlier bits.
Examples of systems using convolutional coding (k = 15, efficiency = 1/6): Mars Pathfinder, Mars Exploration Rover, Cassini Probe
Each incoming binary digit is represented by two outgoing digits. Therefore, the coder efficiency = 1/2
Information bits
Code bits
XOR
XOR

## Slide 30: Turbocodes
C. Berrou, A. Glavieux, P. Thitimajshima, “Near Shannon Limit Error-Correcting Coding and Decoding: Turbo Codes,” IEEE ICC ’93
Turbocodes are generated by a parallel connection of two or more convolutional coders along with an interleaving circuit

## Slide 31: Turbocodes Coding and Decoding
Simple coder 1
Simple coder 2
Simple decoder 1
Simple decoder 2
Channel
Inter- leaver
Information
Decoded information
Iterations
Application example: UMTS

## Slide 32: Line Codes: Expected Features
Elimination of the DC component
Possibility of recreation of the clock frequency in the receiver based on the incoming signal
Error detection
Lowering of the used bandwidth
Increasing robustness against errors

## Slide 33: Line Codes
0
1
0
0
0
0
1
1
0
0
0
0
0
0
1
1
NRZ
P
V
V
AMI
HDB-3
V: violation bit P: parity bit
Notes: Grahame Smillie, Analogue and Digital Communication Techniques, Arnold, London 1999
The violation bit is a bit that violates the AMI principle. The parity bit is not a valid mark but is a bit that is inserted into the bit stream to force the violation bit to assume a particular polarity.
When there are more than three consecutive logic 0 states then the fourth consecutive space is made into a violation bit.
Rule 1. The violation bit must assume the polarity of the valid mark (i.e. Mark or parity bit) that immediately precedes it.
Rule 2. The successive violation must assume a polarity that is opposite to the violation that immediately precedes it.
Rule 3. If there is no valid mark to force a violation bit to have the opposite polarity to the violation that immediately precedes it the a parity bit is used to force the violation to assume the opposite polarity.
Rule 4. The number of spaces between a valid mark and a violation bit is 3.
Rule 5. The number of spaces between a parity bit and a violation bit is 2.

## Slide 34: Coding for Security
Cryptography (gr. secret writing) is the mathematical scrambling of data so that only someone with the necessary key can unscramble it
Cryptography allows secure transmission of private information over insecure channels (e.g., packet-switched networks)
Cryptography also allows secure storage of sensitive data on any computer

## Slide 35: Cryptography
Secret-key algorithm
Text
Ciphered text
Public-key algorithm
Text
Text
Text
Cipher using
a secret key
Ciphered text
Cipher using
a public key
Decipher using
the secret key
Decipher using
the private key

## Slide 36: Coding for Security
Steganography (gr. protected writing) is the art and science of writing hidden messages in such a way that no one, apart from the sender and intended recipient, suspects the existence of the message
The advantage of steganography, over cryptography, is that messages do not attract attention to themselves.

## Slide 37: Conclusion
Source coding
Error detecting and error correcting coding
Channel coding
Line coding
Coding for security

## Slide 38: Thank you very much for your attention