## Slide 1: Transmission Systems
Andrzej Jajszczyk
Introduction to Telecommunications
E&T, 2020/2021, Lecture 11

## Slide 2: Outline
Introduction
PDH Systems
SDH Systems
Network Survivability
Conclusion

## Slide 3: An Example of a PDH System: PCM 30/32
-
1
2
3
28
29
30
15
-
16
...
...
Frame
User channel
0
1
2
3
29
30
31
15
16
17
...
...
Time slot
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Multiframe
Frame
1
2
3
4
5
6
7
8
Bit
Notes: Plesiochronous Digital Hierarchy

## Slide 4: Multiplexing Structure in European PDH Systems
8 Mbit/s
2 Mbit/s
34 Mbit/s
140 Mbit/s
34 Mbit/s
8 Mbit/s
2 Mbit/s
2 Mbit/s
140 Mbit/s
…
64 kbit/s
1
2
3
30

## Slide 5: Limitations of PDH Systems
Differences in PDH standards (European, American, Japanese)
  Differences in bit rates at different multiplexing hierarchy levels
  Different frame structures
  Differences in signal coding
  Differences in synchronization methods
High costs of tributary services related to, e.g., extracting of low bit-rate signals from high bit-rate signals
Technology closely related to voice transport

## Slide 6: Limitations of PDH Systems
Limited space in the frame to send management signals and, as the result, problems with fast network reconfiguration
No uniform standard for the optical interface
A large variety of hardware and lots of devices resulting in low reliability and high power consumption
High system costs

## Slide 7: Origins of SDH
SONET (Synchronous Optical NETwork) — USA (ANSI)
SDH (Synchronous Digital Hierarchy) — CCITT (1988)
Synchronous Digital Hierarchy (SDH): The SDH is a hierarchical set of digital transport structures, standardized for the transport of suitably adapted payloads over physical transmission networks (ITU-T G.707)
Notes: ANSI - American National Standards Institute

## Slide 8: Features of SDH (1)
Synchronous systems
Simplicity of multiplexing and demultiplexing
Smaller required buffers (than in PDH) because of the existence of the pointer mechanism
Simplified network management
Existence of centralized network control mechanisms
Ease of network reconfiguration in case of failures (also self-healing)
Better network resource utilization
Ease of implementation in existing networks

## Slide 9: Features of SDH (2)
Interoperability of European and American systems
Optical interface standard (ITU-T G.957)
Possibility to define new multiplexing hierarchy levels in future
Possibility to send different signal types
Uniformity and modularity of equipment
High reliability of SDH network
Lower operations costs (than in PCM) and better quality indicators
Economic viability of high bit-rate systems

## Slide 10: Cross-Connecting of Lower-Order Streams
1
2
3
.
.
.
n-1
n
1
2
3
.
.
.
n-1
n
1
2
3
.
.
.
n-1
n
1
2
3
.
.
.
n-1
n
Multistage multiplexing
to higher order systems
Multistage
demultiplexing
to lower order
systems
PDH crossconnect
PDH stream with n lower-order streams
SDH stream with n lower-order streams
SDH crossconnect

## Slide 11: Access to Lower-Order Streams
SDH frame
Start
Start
Start
Start
Start
Pointers
Space allocated for lower-order streams
Frame delimiter
Start
PDH frame
Start
Start
Start
Start
Start
Space allocated for lower-order streams

## Slide 12: Multiplexing: Basic Notions
Section: A part of the transmission path between two neighboring network elements performing regeneration or multiplexing
Path: A virtual channel between source and destination nodes used to transmit virtual containers

## Slide 13: SDH: Virtual Container (G.707)
Virtual container-n (VC-n): A virtual container is the information structure used to support path layer connections in the SDH. It consists of information payload and Path Overhead (POH) information fields organized in a block frame structure which repeats every 125 or 500 s
Two types of virtual containers:
  Lower order virtual container-n: VC-n (n =1, 2, 3)
  Higher order virtual container-n: VC-n (n =3, 4)
Container-n (n =1-4): A container is the information structure which forms the network synchronous information payload for a virtual container

## Slide 14: SDH: Tributary Unit (G.707)
Tributary unit-n (TU-n): A tributary unit is an information structure which provides adaptation between the lower order path layer and the higher order path layer. It consists of an information payload (the lower order virtual container) and a tributary unit pointer which indicates the offset of the payload frame start relative to the higher order virtual container frame start
The TU-n (n =1, 2, 3) consists of a VC-n together with a tributary unit pointer

## Slide 15: SDH: Administrative Unit (G.707)
Administrative unit-n (AU-n): An administrative unit is the information structure which provides adaptation between the higher order path layer and the multiplex section layer. It consists of an information payload (the higher order virtual container) and an administrative unit pointer which indicates the offset of the payload frame start relative to the multiplex section frame start

## Slide 16: SDH: Synchronous Transport Module (G.707)
Synchronous Transport Module (STM): An STM is the information structure used to support section layer connections in the SDH. It consists of information payload and Section Overhead (SOH) information fields organized in a block frame structure which repeats every 125 s
A basic STM is defined at 155 520 kbit/s. This is termed STM-1. Higher capacity STMs are formed at rates equivalent to N times this basic rate. STM capacities for N = 4, 16, 64, 256 are defined; higher values are under consideration

## Slide 17: SDH and SONET Rates
SDH | SONET | Optical | Line rate Mbit/s
STM-0 | STS-1 | OC-1 | 51.84
STM-1 | STS-3 | OC-3 | 155.52
STM-4 | STS-12 | OC-12 | 622.08
STM-16 | STS-48 | OC-48 | 2488.32
STM-64 | STS-192 | OC-192 | 9953.28
STM-256 | STS-768 | OC-768 | 39813.12

## Slide 18: Multiplexing in SDH Hierarchy
POH: Path overhead
SOH: Section overhead
STM-N
VC-4
Higher order virtual containers
n  VC-4 + SOH
SOH
Container
Payload
POH
Virtual container
POH
Lower order virtual containers
POH
POH
POH
POH

## Slide 19: Multiplexing Structure by ITU-T
STM-N
AUG
N
AU-4
VC-4
AU-3
VC-3
TUG-3
C-4
TU-3
VC-3
TU-2
VC-2
TU-12
VC-12
TU-11
VC-11
C-3
C-2
C-12
C-11
TUG-2
3
3
1
7
3
4
140 Mbit/s
45 Mbit/s
34 Mbit/s
6 Mbit/s
2 Mbit/s
1.5 Mbit/s
Multiplexing
Mapping
Aligning
Pointer processing
1
7
Notes: TU – tributary unit
TUG – tributary unit group
AU – Administrative Unit
AUG – Aministrative Unit Group

## Slide 20: Multiplexing Structure in Poland
STM-N
AUG
N
AU-4
VC-4
TUG-3
C-4
TU-3
VC-3
TU-12
VC-12
C-3
C-12
TUG-2
3
7
140 Mbit/s
2 Mbit/s
34 Mbit/s
1
1
Multiplexing
Mapping
Aligning
Pointer processing

## Slide 21: STM-1 Module Structure
RSOH
PTR-AU
MSOH
Payload
9 columns
261 columns
3 rows
1 row
5 rows
RSOH Regeneration Section Overhead
MSOH Multiplex Section Overhead
PTR-AU Pointer of Administrative Unit

## Slide 22: STM-1 Module Structure
H1
Y
Y
H2
1
1
H3
H3
H3
AU-4 pointer structure
Pointer-AU
A1
A2
B1
D1
D2
E1
A2
A2
A1
A1
C1
F1
D3
B2
B2
B2
D4
D7
D10
Z1
Z1
Z1
Z2
Z2
E2
Z2
D12
D9
D6
K2
K1
D5
D8
D11
STM-1
RSOH
MSOH
For national use
1
9
270
VC-4
J1
B3
C2
G1
F2
H4
Z3
Z4
Z5
TUG-3

## Slide 23: STM-4 Frame Structure
9
261
9
261
9
261
9
261
STM-1 signal A
STM-1 signal B
STM-1 signal C
STM-1 signal D
36 Columns
1044 columns
STM-4
Overhead Section

## Slide 24: Terminal Multiplexers (TMX)
G.703
Type I.1
STM-N
Type I.1: fixed assignment of PDH signals in the STM-N
G.703
Type I.2
STM-N
Type I.2: flexible assignment of PDH signals in the STM-N
Terminal multiplexers introduce signals to SDH networks

## Slide 25: Line Multiplexers (LMX)
Type II.1
STM-M
STM-N
Type II.1: fixed assignment of VC-3/VC-4
N > M
STM-M
Type II.2
STM-N
Type II.2: flexible assignment of VC-3/VC-4
N > M
Line multiplexers allow multiplexing of several STM-M streams into a single STM-N stream

## Slide 26: Add/Drop Multiplexers (ADM)
STM-M
Type III.1
STM-M
Type III.1: stream sources other than SDH
G.703
STM-M
Type III.2
STM-M
Type III.2: SDH stream sources
M > N
STM-N
Add/drop multiplexers allow to pick out one or more low-speed streams from a high-speed stream and add one or more low-speed streams to a high-speed stream

## Slide 27: Digital Crossconnect (DCS, DXC)
Digital Crossconnect: Network element, which provides automatic cross-connection of a digital signal or its constituent parts
STM-N
STM-M

## Slide 28: SDH/SONET Enhancements
Current SDH/SONET
  SDH/SONET (Synchronous Digital Hierarchy / Synchronous Optical Network) is a widely used, well-understood, mature and standardized technique
  Since it was initially designed for optimising the transport of 64-kb/s-based TDM services, a rigid capacity of payload as well as a coarse fixed-rate multiplexing hierarchy was defined
SDH/SONET enhancements
  Virtual Concatenation
  Link Capacity Adjustment Scheme
  Generic Framing Procedure

## Slide 29: Contiguous Concatenation
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Empty STM-16 signal
VC-4 #1
VC-4 #2
VC-4 #3
VC-4 #4
VC-4 #5
VC-4 #6
VC-4 #7
12
STM-16 signal with two VC-4-4cs and seven VC-4s
VC-4-4c#1
VC-4-4c#2
VC-4 #1
6
VC-4 #3
8
VC-4 #5
10
VC-4 #7
12
STM-16 signal with two VC-4-4cs and four VC-4s
VC-4-4c#1
VC-4-4c#2
VC-4 #1
11
VC-4 #3
9
VC-4 #5
10
VC-4 #7
12
Re-groomed STM-16 signal with two VC-4-4cs and four VC-4s
VC-4-4c#1
VC-4-4c#2
VC-4 #1
VC-4 #3
VC-4 #5
VC-4 #7
STM-16 signal with three VC-4-4cs and four VC-4s
VC-4-4c#1
VC-4-4c#2
VC-4-4c#3

## Slide 30: Principle of Virtual Concatenation
By the use of Virtual Concatenation (VC) technique, SDH/SONET may be improved to better meet today’s requirements, e.g., high switching granularities
Virtual concatenation was invented to allow flexible concatenation of several SDH/SONET payloads. It provides effective use of SDH/SONET capacity
Virtually concatenated payloads constitute a Virtual Concatenation Group (VCG). Members of VCG, as opposed to contiguous concatenation, may not reside in the same STM-N/OC-N contiguously. They may even reside at different STM-N/OC-N interfaces. They are treated within the network separately and independently. As a consequence, they may reach the destination through various routes

## Slide 31: Features of Virtual Concatenation
Intermediate nodes do not need to handle virtual concatenation. The VC functionality must be implemented only at path termination nodes. This feature makes it possible to deploy virtual concatenation on legacy SDH/SONET equipment of existing networks
Differences in the delay of an individual concatenated signal may occur due to pointer processing at intermediate nodes. Compensation of differential delays is handled at the destination node

## Slide 32: Bandwidth Efficiency of Virtual Concatenation
Data signal
SDH without VC
SDH with VC
Payload mapping
Bandwidth efficiency
Payload mapping
Bandwidth efficiency
Ethernet 10 Mbit/s
VC-3
21%
VC-11-7v
89%
Fast Ethernet 100 Mbit/s
VC-4
67%
VC-11-64v
98%
Gigabit Ethernet 1 Gbit/s
VC-4-16c
42%
VC-4-7v
95%
Notes: VC-3 – 45 Mbit/s
VC-4 – 140 Mbit/s

## Slide 33: Benefits of Virtual Concatenation
Scalability SDH pipes can be sized to match the desired data rate and thereby avoid unnecessary waste
Efficiency Virtually concatenated channels are more easily routed through a network and eliminate stranded bandwidth
Compatibility Virtual concatenation works across legacy networks
Resiliency Individual members of a virtually concatenated channel are recommended to be routed as diversely as possible across a network. So if one link goes down, the others are likely to be operational

## Slide 34
Network Survivability

## Slide 35: Basic Recovery Methods
Protection Switching to a pre-established recovery path or path segment after the occurrence of a fault
Restoration Establishing new paths or path segments on demand for restoring traffic after the occurrence of a fault

## Slide 36: Line Level Protection Techniques
TMX
TMX
Working line
Protection line
Linear 1+1
TMX
TMX
Working lines
Protection line
Linear 1:N
In 1:N protection low priority traffic can be carried over the protection line when that line is not carrying traffic for a failed working line

## Slide 37: Example 1+1 Line Protection
Tx
Rx
1+1 protection
Splitter
2 wavelength WDM line system
Fast protection
No signaling required between end-points
High cost (duplication of wavelengths and corresponding transponders)
Tx: Transceiver
Rx: Receiver
Switch

## Slide 38: Example 1 : 1 Line Protection
Tx
Rx
1:1 protection
1:1 protection
Fast protection (slower than 1+1)
Signaling required between end-points
High cost (duplication of wavelengths corresponding transponders) But: possibility for low priority pre-emptable traffic

## Slide 39: Protection in Ring Networks
1
3
5
4
2
Fibre cut

## Slide 40: Local (Link-based) Protection Scheme for MPLS Networks
Backup for M1-M2 hop
M1
M2
M3
M4
M5
M7
M6
Backup for M4-M5 hop
Primary lambda LSP (M1-M7)

## Slide 41: Global (Path-based) Protection Scheme for MPLS Networks
Backup lambda LSP (M1-M7)
M1
M2
M3
M4
M5
M7
M6
Primary lambda LSP (M1-M7)

## Slide 42: Example Restoration
Before failure
Ingress node
Egress node
Source: Colle, IEEE JSAC, Jan. 2002

## Slide 43: Example Restoration
Link data base
Faulty link deletion
After failure
Fault notification
Ingress node
Egress node
Source: Colle, IEEE JSAC, Jan. 2002

## Slide 44: Example Restoration
After failure
New path segment calculation
Ingress node
Egress node
Source: Colle, IEEE JSAC, Jan. 2002

## Slide 45: Preconfigured Protection Cycles (p-cycles)
a p-cycle forms a closed path (loop) in the network
p-cycles are created on the basis of only spare resources
two types of links are protected
  on-cycle links
  straddling links

## Slide 46: Preconfigured Protection Cycles (p-cycles)

## Slide 47: Preconfigured Protection Cycles (p-cycles)
More efficient protection

## Slide 48: Preconfigured Protection Cycles (p-cycles)
P. Chołda, A. Jajszczyk, “Reliability assessment of optical p-Cycles”, IEEE/ACM Transactions on Networking, vol. 15, no. 6, December 2007, pp. 1579-1592

## Slide 49: Conclusion
PDH Systems
SDH Systems
Network survivability

## Slide 50: Have a Happy Holiday Season!