## Slide 1
Amplitude & Frequency Modulations
„Signals & Systems” Zdzisław Papir
Telecommunication system
Definition of modulation
Spectra of information source signals
Purposes of using modulation
The lunch for free does not exist
Definition of demodulation/detection
Classification of modulations
Amplitude Modulation (AM)
Frequency Modulation (FM)

## Slide 2
„Signals & Systems” Zdzisław Papir
Lowpass filter
Mo- dulator
Bandpass filter
Bandpass filter
Demo- dulator
Lowpass filter
Transmitter
Receiver
Transmission channel
Telecommunication system
AWGN – Additive White (Wideband) Gaussian Noise
AWGN

## Slide 3
Definition of modulation
„Signals & Systems” Zdzisław Papir
Modulation involves three signals:
information carrying signal = modulating signal x(t)
carrier c(t)
modulated signal φ(t)
Modulation is mapping of information signal x(t) into one of the parameters of the carrier c(t).
The output signal φ(t) is called the modulated signal.
MODULATOR
φ(t)
x(t)
c(t)

## Slide 4
Amplitude Modulation (AM-DSB)
(AM-Double SideBand)
„Signals & Systems” Zdzisław Papir
MODULATOR

## Slide 5
Phase Modulation (PM)
„Signals & Systems” Zdzisław Papir
MODULATOR

## Slide 6
Frequency Modulation (FM)
„Signals & Systems” Zdzisław Papir
MODULATOR

## Slide 7
Spectra of information source signals
„Signals & Systems” Zdzisław Papir
Voice - baseband – up to several kHzs
Sound - baseband – up to tens of kHzs
Video – baseband – up to several MHzs
Raw data – baseband – up to ...?

## Slide 8
Purposes of using modulation
„Signals & Systems” Zdzisław Papir
1. Access to different parts of the electromagnetic spectrum
Microwave - MHzs
Copper plant – baseband up to 10 MHz
Fiber – narrow frequency window at THzs
Satellite - GHzs

## Slide 9
„Signals & Systems” Zdzisław Papir
2. Better noise immunity of transmission
TRANSMITTER
RECEIVER
TRANSMISSION CHANNEL
wideband (white) noise
modulation
detection
improvment of the Signal to Noise Ratio (SNR)
SNR (modulation) > SNR (baseband system)
SNR
Purposes of using modulation

## Slide 10
„Signals & Systems” Zdzisław Papir
Frequency
Frequency (FDM)
Time (TDM)
interleaved signal spectra
interleaved data blocks
Purposes of using modulation
3. Division Multiplex
Time

## Slide 11
The lunch for free does not exist
„Signals & Systems” Zdzisław Papir
#1 Access to different parts of the electromagnetic spectrum
#2 Better noise immunity of transmission
#3 Frequency and/or Time Division Multiplex of transmission channels
#4 SPECTRUM WIDENING
B [Hz] or W [rad/s] – bandwidth of the modulated signal
fm [Hz] or ωm [rad/s] – bandwidth of the modulating signal
bandwidth widening (expansion) coefficient

## Slide 12
Definition of Demodulation
„Signals & Systems” Zdzisław Papir
Modulation is MAPPING the information signal onto the carrier.
MODULATOR
φ(t)
x(t)
c(t)
DEMODULATOR
φ(t)
x(t)
c(t)
Demodulation is STRIPPING the information signal from the modulated carrier.

## Slide 13
Definition of Detection
„Signals & Systems” Zdzisław Papir
DETECTION
φ(t) + ANGN
x(t) + noise
c(t)
Detection is STRIPPING the information signal from the carrier in a noisy environment (demodulation of signal corrupted by ANGN).

## Slide 14
„Signals & Systems” Zdzisław Papir
Classification of Modulations
MODULATOR
φ(t)
x(t)
c(t)
Digital - Analog
Digital - Analog
Analog waveform
sin or cos waveform (A)
Digital waveform
sequence of pulses (D)

## Slide 15
„Signals & Systems” Zdzisław Papir
Classification of Modulations
carrier
information signal
D
D
A
A
Sampling theorem
PAM
PFM
PDM
Keying
ASK
PSK
FSK
MSK
GMSK
Line codes
NRZ
Miller
HDB
PRS
AM
FM
SSB
QAM
Classics
DSB
0 0 1 0 1 0 1…

## Slide 16
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM)
Modulation (AM-DSB)
carrier
no overmodulation

## Slide 17
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM) (no overmodulation: 1 + kx(t) ≥ 0
t
Positive peaks of the AM signal do follow the modulating signal. The „envelope” of positive AM peaks coincides with the modulating signal.

## Slide 18
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM) (overmodulation: 1 + kx(t) ≤ 0)
A0│1 + kx(t)│
Positive peaks of the AM signal do not follow the modulating signal.

## Slide 19
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM) –
single tone
Single tone modulation: x(t) = acoswmt
jAM(t)=A0(1 + kx(t)) cosw0t
jAM(t)=A0(1 + ka coswmt) cosw0t
ka = m – modulation (depth) index
Determine the phasor diagram for the single tone AM signal.

## Slide 20
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM) – single tone
t
mA0
+A0(1+m)
mA0
+A0(1m)
A0

## Slide 21
„Signals & Systems” Zdzisław Papir
Amplitude Modulation (AM)
X(w)
FAM(w)
w
w0-wm w0 w0+wm
wm
-wm
w

## Slide 22
„Signals & Systems” Zdzisław Papir
AM Detection (demodulation)
Two possible detection techniques:
- Envelope (noncoherent) detection
- Coherent (synchronous) detection

## Slide 23
„Signals & Systems” Zdzisław Papir
AM Envelope (noncoherent) Detection
-x(t)
t
Peak Value Detector (•) & Interpeak Approximation
Low Pass Filter
AM Envelope Detector (no carrier recovery at a receiver is necessary)
envelope

## Slide 24
„Signals & Systems” Zdzisław Papir
Envelope Detection – overmodulation errors
1 +kx(t) < 0
e(t) = A0│1 +kx(t)│

## Slide 25
„Signals & Systems” Zdzisław Papir
AM Coherent (synchronous) Detection
LPF
~x(t)

## Slide 26
„Signals & Systems” Zdzisław Papir
Coherent AM Detection – phase errors
Synchronous operation of both transmitter
and receiver is necessary.

## Slide 27
Longwave Transmitter (Solec Kujawski)
The longwave transmitter Solec Kujawski is a longwave broadcasting facility of the Polish Radio mainly for the AM-LW (long wave) radio broadcasting at the 225 kHz carrier frequency with a bandwidth of 9 kHz.
Longwave transmitter 1.2 MW max power
Two masts of 330 m and 289 m height
„Signals & Systems” Zdzisław Papir
Solec Kujawski

## Slide 28
AM Emissions (radio broadcasting mainly)
LONG WAVES:
30 kHz  300 kHz (10 km  1 km)
AM Emissions:
144 kHz  288 kHz
Distance covered:
1000 km  2000 km
Propagation:
ground wave, skywave
MEDIUM WAVES:
300 kHz  3 MHz (1 km  100 m)
AM Emissions:
522 kHz  1611 kHz
Distance covered:
~100 km
Propagation:
ground wave
„Signals & Systems” Zdzisław Papir

## Slide 29
Amplitude Modulation - - other schemes
AM-DSB
Double SideBand (no carrier)
„Signals & Systems” Zdzisław Papir
AM-VSB
Vestigal SideBand
Nyquist slope
AM-SSB
Single SideBand
AM
AM-DSB+carrier

## Slide 30
Quadrature Amplitude Modulation - QAM
x(t)
cosw0t
sinw0t
y(t)
„Signals & Systems” Zdzisław Papir
Prove that it is possible to simultaneously coherently detect both signals x(t) and y(t).
Recommend the block diagram of the receiver.

## Slide 31
Frequency Modulation (FM)
jFM(t)
-a
0
a
-A0
0
A0
x(t)= acoswmt
„Signals & Systems” Zdzisław Papir

## Slide 32
Frequency Deviation and Modulation Index
Single Tone FM ( x(t) = acoswmt )
„Signals & Systems” Zdzisław Papir
FM Modulation index
FM modulation index Dj shows how much the FM phase angle is deviating around the linear phase trend ω0t.

## Slide 33
Frequency Deviation and Modulation Index
Single Tone FM ( x(t) = acoswmt )
„Signals & Systems” Zdzisław Papir
Modulation index
Frequency deviation
FM frequency deviation index Dω shows how much the FM instantaneous frequency is deviating around the carrier fequency ω0.

## Slide 34
FM Waves
-A0
0
A0
-A0
0
A0
-A0
0
A0
-a
0
a
x(t)= acoswmt
Dw
1.5 Dw
2.0 Dw
„Signals & Systems” Zdzisław Papir

## Slide 35: Spectrum Analysis of Single Tone FM
„Signals & Systems” Zdzisław Papir

## Slide 36: Spectrum Analysis of Single Tone FM
Jn(Dj) – Bessel’s functions of the 1st kind, n-th order
Exponential Fourier Series
„Signals & Systems”  Zdzisław Papir

## Slide 37: Spectrum Analysis of Single Tone FM
„Signals & Systems”  Zdzisław Papir
Jn(Dj) – Bessel’s functions of the 1st kind, n-th order

## Slide 38: Spectrum Analysis of Single Tone FM
„Signals & Systems”  Zdzisław Papir

## Slide 39: Properties of Bessel’s Functions
„Signals & Systems”  Zdzisław Papir

## Slide 40: Plots of Bessel’s Functions
0
2
4
6
8
10
12
14
16
18
20
-0.5
0
0.5
1
Dj
Jn(Dj)
J0
J7
J5
J3
J10
J1
J2
„Signals & Systems”  Zdzisław Papir

## Slide 41: Values of Bessel’s Functions
„Signals & Systems”  Zdzisław Papir
Jn(Dj)
Each function Jn(Dj) attains its maximum value for some modulation index Dj and then is asymptotically tending to 0, Jn(Dj)→0.

## Slide 42: Line spectrum of a single tone FM
„Signals & Systems”  Zdzisław Papir
A0|Jn(Dj)|
w
w0+4wm
w0-4wm
w0+8wm
w0-8wm
w0+wm
w0
w0-wm
Essential spectra lines

## Slide 43
„Signals & Systems”  Zdzisław Papir
|Jn(Dj)|
w
N(Dj)
w0+4wm
w0-4wm
w0+8wm
w0-8wm
w0+wm
w0-wm
e
Essential lines
FM frequency bandwidth
2N(∆φ) – number of essential lines @ given index ∆φ & threshold ε

## Slide 44: Spectrum of FM (Carson’s rule)
where:
„Signals & Systems”  Zdzisław Papir
is the number of „essential” spectra lines, so:

## Slide 45: # essential spectrum lines N()
0
2
4
6
8
10
12
14
16
18
20
22
24
26
0
2
4
6
8
10
12
14
16
18
20
22
Dj
N()
Dj+2
Dj+1
e=0,01
e=0,1
e=0,05
The spectrum line is considered to be essential whenever its amplitude exceeds some predefined level eA0, 0,01 < e < 0,1.
„Signals & Systems”  Zdzisław Papir

## Slide 46: # essential spectrum lines N()
0
2
4
6
8
10
12
14
16
18
20
22
24
26
0
2
4
6
8
10
12
14
16
18
20
22
24
26
Dj
N()
P=99,8%
P=90%
P=98%
Dj+1
The number of essential spectrum lines is derived from the fractional power of the FM signal.
„Signals & Systems”  Zdzisław Papir

## Slide 47
Spectrum of FM – rule of thumb
where:
„Signals & Systems”  Zdzisław Papir
is the number of essential spectra lines, so:

## Slide 48
FM stereo broadcasting
„Signals & Systems”  Zdzisław Papir