## Slide 1: PULSE CODE MODULATION (PCM) (A/D conversion)

## Slide 2: Agenda
Pulse Code Modulation (quantization)
Quantization process
Quantization noise and mean-squared error
Signal to Quantization Noise Ratio
Non-uniform quantization (compression)
Optimal quantization characteristic
Compression A and compression µ
Summary
„Signals & Systems”  Zdzisław Papir

## Slide 3: Pulse Code Modulation
„Signals & Systems”  Zdzisław Papir
SAMPLING
QUANTIZATION
CODING
x(t)
PCM
Nyquist theorem
x(nT0)
x(nT0) ≈ vk k = 0, 1,…, K-1
k10 → k2
Sample approximation by a fixed level
Binary encoding of a decimal number of quantization level

## Slide 4: Quantization idea
„Signals & Systems”  Zdzisław Papir
Analog signal:
values are changing fluently
infinite numer od signal values in a limited range
human senses can differentiate among finite numer of signal values
Approximation of an analog signal by a signal with finite number of levels

## Slide 5: (Amplitude) quantization
„Signals & Systems”  Zdzisław Papir
(amplitude) quantization is approximation of a sample x(nT0 ) of an information signal x(t) at the instant t = nT0 by a quantization level vk which belongs to a finite set of possible levels {vk, k = 0, 1,…, K – 1}.
T0 is a sampling period according to the Nyquist theorem.

## Slide 6
„Signals & Systems”  Zdzisław Papir
Analog signal x(t)
Quantized signal v(t) (6 quantization levels)
Signal quantization
Signal quantization
Quantization levels
Signal samples
Quantization thresholds
0
1
2
3
4
5
Number of a quantization level (0, 1,…,5)

## Slide 7
Signal sampling
Signal quantization
„Signals & Systems”  Zdzisław Papir
Number of a quantization level (0, 1,…11)
Analog signal x(t)
Quantized signal v(t) (12 quantization levels)
Quantization levels
Signal samples
Quantization thresholds

## Slide 8: Coding
„Signals & Systems”  Zdzisław Papir
x(nT0) ≈ vk, k = 0, 1,…, K-1
Number of quantization levels K is a power of 2:
K = 2R; decimal numer of a quantization level k10 can be encoded binary k2:
Example: k10 = 13 → k2 = (1, 0, 1, 1)
T0
1 0 1 1
Binary encoding of a decimal number of quantization level k10 → k2

## Slide 9: Quantization model
„Signals & Systems”  Zdzisław Papir
δk = xk+1 – xk – length of k-the quantization level
k = 0, 1, …, K-1
δk = δ = const – uniform quantization
δ – step size of a uniform quantizer
xk
xk+1
xk-1
k-th quantization level (xk, xk+1]
K – number of quantization levels
k = 0, 1, …, K-1
k-th quantization level vk
K – number of quantization levels
k = 0, 1, …, K-1
xk

## Slide 10: Quantizer (characteristic)
„Signals & Systems”  Zdzisław Papir
δk = xk+1 – xk length of a quantization level
xk+1
xk
vk
vk+1
vk-1
xk-1 < vk < xk
vk

## Slide 11: Quantization noise
QUANTIZAION NOISE
analog signal – quantized signal
ANALOG SIGNAL
QUANTIZED SIGNAL
„Signals & Systems”  Zdzisław Papir

## Slide 12: Quantization error
Quantization is related with an irretrievable loss of information of an exact value of a signal sample. Difference between the sample and its quantizewd level is defined as a quantization error.
„Signals & Systems”  Zdzisław Papir
xk
xk+1
xk-1
vk – quantization level
x – signal sample (analog)
Quantization error

## Slide 13: Quantization error
„Signals & Systems”  Zdzisław Papir
Uniform quantizer in the range [-xMAX, +xMAX]:
K – numer of quantization levels
δ – step size
xk
xk+1
vk – quantization level
δ
Dense (K↑) uniform quantization:

## Slide 14: Quantization error
„Signals & Systems”  Zdzisław Papir
Quantization error for a dense uniform quantization (number of quantization levels K is large enough):
is a random variable with a uniform pdf.

## Slide 15: Mean-squared quantization error
„Signals & Systems”  Zdzisław Papir
Mean-squared quantization error for a dense uniform quantization (number of quantization levels K is large enough):

## Slide 16
Each sample is reperesented by a codeword of R bits:
„Signals & Systems”  Zdzisław Papir
Mean-squared quantization error

## Slide 17: Signal to Quantization Noise Ratio
„Signals & Systems”  Zdzisław Papir
Extending a codeword by 1 bit increases the Signal to Quantization Noise ratio by 6 [dB].
We assume that the quantization noise power Q is equal to the mean-squared uniform quantization error:
Information signal power:

## Slide 18: Non-uniform quantization
„Signals & Systems”  Zdzisław Papir
Non-uniform quantization:
low signal values are quantized more accurate
quantization step size follows a level of a signal sample
less numer of quantization levels as compared to a uniform quantization

## Slide 19: Idea of non-uniform quantization
-xmax
+xmax
f(x) – information signal pdf
-xmax
-xmax
+xmax
„Signals & Systems”  Zdzisław Papir
+xmax
Uniform quantization
Non-uniform quantization
Non-uniform quantization provides more accurate quantization of low level samples which appear more frequently.

## Slide 20: Non-uniform quantization error
„Signals & Systems”  Zdzisław Papir
δk = xk+1 – xk – step size for the k-th quantization interval
pk = Pr{xk < x < xk+1}
Mean-squared quantization error for a dense uniform quantization (number of quantization levels K is large enough):
Mean-squared quantization error for a dense non-uniform quantization (number of quantization levels K is large enough):

## Slide 21: Non-uniform quantization – approach
Ideal solution (adaptive quantization) – quantizator range xMAX follows range of an information signal xmax:
Adaptive quantization provides constant Signal to Quantization Noise Ratio.
„Signals & Systems”  Zdzisław Papir
Let:

## Slide 22: Signal compression
COMPRESSION
+
UNIFORM QUANTIZATION
=
NON-UNIFORM QUANTIZATION
Compression
Quantization
Coding
x(t) T0
y(t)
Non-linear compression and subsequent uniform quantization results in a non-uniform quantization
„Signals & Systems”  Zdzisław Papir
y
1
1
x
Compression function
y = y(x)

## Slide 23: Compression – quantization error
„Signals & Systems”  Zdzisław Papir
y
1
1
x
Compression function
y = y(x)

## Slide 24: Compression – SQR
„Signals & Systems”  Zdzisław Papir
SQR = const ?

## Slide 25: Compression – SQR
„Signals & Systems”  Zdzisław Papir
Constant SQR requests:

## Slide 26: Compression function for SQR = const
Relative size of quantization intervals is constant.
Quantization step size follows a level of a signal sample.
„Signals & Systems”  Zdzisław Papir
x
y
1
1
e-k

## Slide 27: Compression μ (μ = 100…300)
„Signals & Systems”  Zdzisław Papir
Compression A (A = 100…300)
Compression functions µ and A are linear for low level signal values and logarithmic for high ones.

## Slide 28: Compression functions μ and A
μ=0
μ=5
μ=100
A=100
A=2
A=1
„Signals & Systems”  Zdzisław Papir
Quantization of low level signal values is very accurate as compression functions are very steep (slop angle ~87o…88o).

## Slide 29: SQR - compression A, weak signals
Compression A for weak signals is linear:
Quantization at a linear section of a compression function does not provide a constant SQR for weak signals, however, SQR grows by a comprresion gain g[dB].
„Signals & Systems”  Zdzisław Papir
Weak signals are quantized uniformely, however, a step size decreases by a factor g = A/(1 + lnA), so the number of quantization levels grows by the same factor: K → gK.
SQR for a uniform quantization equals:

## Slide 30: SQR – compression A, strong signals
Strong signals are compressed logaritmicaly:
„Signals & Systems”  Zdzisław Papir
SQR for a logarithmic compression equals:
and does not depend on a signal level.

## Slide 31: SQR vs. signal level, compression A
„Signals & Systems”  Zdzisław Papir
10
20
30
40
0
-10
-20
-30
-40
-50
Compression A
Uniform quantization
Compression gain g = 25[dB]
SQR[dB]
P[dB]

## Slide 32: Compression & expansion
Accurate recovering samples in a receiver requests for sample expansion (inverse operation to a compression).
Combined compression and expansion is called companding.
„Signals & Systems”  Zdzisław Papir

## Slide 33: Linear-logarithmic compression Summary
Weak signals are quantized more precisely as compared to strong signals.
Linear-logarithmic compression results in a constant Signal to Quantization Ratio (SQR)over a wide range of signal levels.
Compression results in decreasing transmission rate at the retained SQR level.
Compression of weak signals increases SQR by a compression gain.
Compression shortens length of codewords.
„Signals & Systems”  Zdzisław Papir