## Slide 1: Power Properties of Signals
„Signals & Systems” Zdzisław Papir
Definitions of energy and power of a signal
Signal energy and power in the frequency domain
Autocorrelation function of an energetic signal
Autocorrelation function of a power signal
Taxonomy of signals
Acf and energy/power spectrum properties
Acf definitions – various signals
Acf as a measure of signal similarity

## Slide 2: Signal Energy Definition
„Signals & Systems” Zdzisław Papir
i(t) = x(t)
u(t) = x(t)
E
R = 1 
Signal is energetic whenever E < .
Energetic signals have spectral representation (Fourier transform does exist).

## Slide 3
Signal energy in the frequency domain
„Signals & Systems” Zdzisław Papir
Parseval theorem
Spectral energy density (energy spectrum):
indicates how the total signal energy is distributed over frequencies.
According to the Parseval theorem signal energy can be determined either in the time or frequency domain.

## Slide 4
Parseval theorem - example
According to the Parseval theorem signal energy can be determined either in the time or frequency domain.
„Signals & Systems” Zdzisław Papir
Find the energy of the signal x(t) in the time
and frequency domain.

## Slide 5
„Signals & Systems” Zdzisław Papir
Signal energy in a given frequency bandwidth
Energy up to some frequency
Energy in a bandwidth
Total energy

## Slide 6: Fractional energy
„Signals & Systems” Zdzisław Papir
Fractional energy Ef(ω) indicates the fraction of the total signal energy contained in a bandwidth [0, ω].

## Slide 7: Fractional energy
frequency f
rectangular pulse – fractional energy
amplitude spectrum
fractional energy
„Signals & Systems” Zdzisław Papir

## Slide 8
Autocorrelation function of an energetic signal
„Signals & Systems” Zdzisław Papir

## Slide 9
„Signals & Systems” Zdzisław Papir
Autocorrelation f. - example
Find the autocorrelation function (acf) of the signal x(t):

## Slide 10
Acf - measure of signals similarity
„Signals & Systems” Zdzisław Papir
Error of approximation x(t) by ρv(t)
ρ coeff. – basic property
-0.5
0
0.5
0
0.2
0.4
0.6
0.8
1
1.2
1.4
time t
x(t)

## Slide 11
„Signals & Systems” Zdzisław Papir
Correlation - measure of signal similarity
Correlation coefficient  is a measure of similarity of two signals x(t) and (t).
Schwarz inequality

## Slide 12
„Signals & Systems” Zdzisław Papir
The  coefficient is called a correlation (similarity) coefficient for two signals x(t) and (t).
Correlation - measure of signal similarity
Normalization of
x(t) and (t)
Schwarz inequality:
results in:

## Slide 13
„Signals & Systems” Zdzisław Papir
Correlation coefficient - example

## Slide 14
„Signals & Systems” Zdzisław Papir
Correlation - measure of signal similarity
Correlation coefficient has to involve a time delay (shift):
Intercorrelation function of two signals x(t) and(t):
Autocorrelation function of signal x(t):
correlation = 1
correlation = 0

## Slide 15
„Signals & Systems” Zdzisław Papir
Power signals meet the condition P < . Power signals possess a Fourier transform if Dirac delta is adopted.
Within „regular” signals the only known deterministic
power signals are periodic.
Other power signals: sgn(t), 1(t), dc …
i(t) = x(t)
u(t) = x(t)
P = E/T
R = 1 
Signal Power Definition
Periodic signals possess the Fourier transform:

## Slide 16: Time averaging (what does it mean?)
„Signals & Systems” Zdzisław Papir
xi – signal sample
i – sample number
N – # all samples

## Slide 17: Power of a periodic signal
„Signals & Systems” Zdzisław Papir
Power of a periodic signal is equal to its power calculated over its single period.
Time averaging of a whatever periodic quantity (over infinite horizon) can be always calculated as a time average over a single period.

## Slide 18: Power of an harmonic signal
„Signals & Systems” Zdzisław Papir

## Slide 19
„Signals & Systems” Zdzisław Papir
Signal power in the frequency domain
Power spectral density
Parseval theorem - analogue

## Slide 20
Autcorrelation function of a periodic power signal
„Signals & Systems” Zdzisław Papir
The only known deterministic power signals are periodic, so is the autocorrelation function:
Periodic signals have Fourier transform (Fourier series).

## Slide 21: Power of a periodic signal in frequency domain
„Signal Theory”  Zdzisław Papir
Total power
of a signal
Parseval Theorem
Fourier series
Fractional power

## Slide 22: Fractional Power
„Signal Theory”  Zdzisław Papir
0
5
10
15
20
25
30
35
0
0.05
0.1
0.15
0.2
kf0
|Xk|
Sawtooth signal – Fourier coefficients
T = 1
t
1

## Slide 23: Fractional power
„Signal Theory”  Zdzisław Papir
0
5
10
15
20
25
30
35
75
80
85
90
95
100
kf0
Pf(k0) [%]
Sawtooth signal – fractional power
T = 1
t
1

## Slide 24: Fractional power (sawtooth signal - 90%)
„Signal theory”  Zdzisław Papir
0
0.5
1
1.5
0
0.2
0.4
0.6
0.8
1
Sawtooth signal approximation
2 harmonics
90% of total signal power
T = 1
t
1

## Slide 25: Fractional power (sawtooth signal - 95%)
„Signal Theory”  Zdzisław Papir
0
0.5
1
1.5
0
0.2
0.4
0.6
0.8
1
Sawtooth signal approximation
4 harmonics
95% of total signal power
T = 1
t
1

## Slide 26: Fractional power (sawtooth signal - 99%)
„Signal Theory”  Zdzisław Papir
0
0.5
1
1.5
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
Sawtooth signal approximation
16 harmonics
99% of total signal power
T = 1
t
1

## Slide 27
„Signals & Systems” Zdzisław Papir
time t
-T/2
xT(t)
+T/2
x(t) – power signal
xT(t) – energy signal
Signal power in the frequency domain

## Slide 28
„Signals & Systems” Zdzisław Papir
Spectral power density (power spectrum):
Signal power in the frequency domain

## Slide 29
Taxonomy of signals
„Signals & Systems” Zdzisław Papir
energy signals
power signals
deterministic signals
random signals (information)
Fourier transform – YES
Energy spectrum – YES
Autocorrelation f. - YES
such signals do not exist
Fourier transform – NO
Power spectrum – YES
Autocorrelation f. - YES
Periodic signals:
Fourier transform – YES Power spectrum – YES
Autocorrelation f. - YES

## Slide 30
„Signals & Systems” Zdzisław Papir
2. Energy (power) spectrum and acf are even functions:
Concept of acf and power (energy) spectrum embraces spectral analysis of all signals types.
1. Energy (power) spectrum is a Fourier transform of an autocorrelation function (acf):
Acf and spectrum properties

## Slide 31
„Signals & Systems” Zdzisław Papir
3. Autocorrelation function is bounded by R(0):
so acf may be a measure of signal selfsimilarity (similarity between a signal and its time-delayed replica):
Acf and spectrum properties
Hint: consider the expression:
Autocorrelation value R(τ = 0) is equal to either energy or power of a signal.
deterministic energy signal
deterministic power signal

## Slide 32
„Signals & Systems” Zdzisław Papir
4. When filtering the energy (power) spectrum is modified
by a squared amplitude-frequency filter characteristic.
Phase-frequency characteristic does not influence the energy (power) spectrum.
Acf and spectrum properties

## Slide 33
„Signals & Systems” Zdzisław Papir
Acf and spectrum properties
The signal x(t) is input to the ideal lowpass filter with the bandwidth ωb. Find the bandwidth ωb such that the output signal energy is equal to ½ of the input signal energy.
The autocorrelation function of some signal is given by:
Find the power spectrum of the process and the fractional power of the process. Find the bandwidth of the proces that contains 50% of the total process power.

## Slide 34
Acf definitions – various signals
„Signals & Systems” Zdzisław Papir
Power random signals
Power deterministic signals
Acf + time averaging
Acf + time and ensamble averaging
Energy signals
Autocorrelation function (acf)

## Slide 35
Summary
Energy or power of a signal can be determined from energy or power spectrum, respectively.
Energy and power spectra are Fourier transforms of corresponding autocorrelation functions acf).
Autocorrelation function is defined in a various manner in different signal classes.
Energy and power spectra posses identical properties being independent of a signal class.
Filtration modifies both energy and power spectra by squared amplitude-frequency function (a-f).
Autocrrelation function is a mesure of signal similarity.3535