## Slide 1
Random signals
Random variable
Moments of a random variable
Random signals
Moments of a random signal
Ergodicity of a random signal
Spectral analysis of a random signal
Summary
Case studies
„Signals & Systems” Zdzisław Papir

## Slide 2
Random variable
„Signals & Systems” Zdzisław Papir
Random variable x is a physical quantity changing in an unpredictable way in a population of objects (ω); fluctuations are described by a cumulative distribution function cpdf (probability density function - pdf).
cumulative probability distribution function - cpdf
probability density function - pdf
x
x

## Slide 3
Probability Density Function (pdf) of a random variable
„Signals & Systems” Zdzisław Papir
Pdf points to either: - preferred values of a random variable,
- dispersion of a random variable around preferred values.
x1
x2
x
x + ∆x
Interval probability for a random variable to take on a specific value

## Slide 4
„Signals & Systems” Zdzisław Papir
Normal random variable
0
+1
+2
-1
+3
-2
-3
Application: modeling Additive White Gaussian Noise (AWGN) corrupting transmission in analog and digital transmission channels.

## Slide 5
„Signals & Systems” Zdzisław Papir
Exponential random variable
time
τ
1
2
3
4
5
6
0
0.5
1
1.5
2
2.5
τ
f(τ)
λ = 1
λ = 2
λ = 3
Application: modeling call (session) interarrival and holding times.

## Slide 6
Erlang random variable
rl
rl
rl
exponential random variables (#r)
„Signals & Systems” Zdzisław Papir
+
+
+

## Slide 7
0.5
1
1.5
2
2.5
3
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
t
a
(
t
)
r = 20
r = 10
r = 5
r = 3
r = 1
„Signals & Systems” Zdzisław Papir
Erlang random variable
Application: modeling performance of call centers

## Slide 8
„Signals & Systems” Zdzisław Papir
Pareto random variable
Application: modeling file sizes
1
2
3
4
5
6
0
0.5
1
1.5
2
2.5
τ
f(τ)
Exp
Pareto
τ - # bytes
file

## Slide 9
„Signals & Systems” Zdzisław Papir
Moments of a random variable
Mean (expected) value of a random variable:
Mean squared value of a random variable:

## Slide 10
„Signals & Systems” Zdzisław Papir
Moments of a random variable
Variance of a random variable:
Standard deviation of a random variable:

## Slide 11
„Signals & Systems” Zdzisław Papir
Standard deviation is a measure of random variable spread around its average value.
x
x
The less the value of a spread coefficient the more the random variable resembles a deterministic value (cx = 0).
Moments of a random variable

## Slide 12
„Signals & Systems” Zdzisław Papir
x(t=const, ω=const) – sample (number)
x(t=const, ω=var) – random variable
x(t=var, ω=const) – path of a random signal
x(t=var, ω=var) – random signal (ensemble of paths)
Practically, we adopt simpler notation x(t) x(t).
Random signals
path, ω1
path , ω2
path, ω3
Randomness is not a seemingly chaotic path of a single observed object (ω) .
Randomness is grasped as an ensemble of paths of several objects ω1, ω2, ω3…
Path observed for an object ω is a deterministic signal (power?, energy?)
x(t) - random signal = = ensemble of paths
x(t) – random signal = random variable moving over time axis

## Slide 13
Pdfs of random signals (stationary)
„Signals & Systems” Zdzisław Papir
Pdf of the 1st order (does not depend on time)

## Slide 14
Pdfs of random signals (stationary)
„Signals & Systems” Zdzisław Papir
Pdf of the 2-nd order (depends on time spacing)

## Slide 15
Moments of a random signal
„Signals & Systems” Zdzisław Papir
The mean values of a stationary random signal
do not depend on time:
Autocorrelation function of a stationary random signal does not depend on a current time t, though it depends on time spacing τ.

## Slide 16
„Signals & Systems” Zdzisław Papir
Moments of a random signal are ensemble (probabilistic) averages as they are calculated for a fixed time instants for an ensemble including all signal paths.
Ergodocity of a random signal
i – path number
N - # all paths
pdf, f(x)

## Slide 17
„Signals & Systems” Zdzisław Papir
Time-averaged moments of a signal are determined for a single signal path.
Ergodicity of a random signal
i – sample number
N – # all samples

## Slide 18
„Signals & Systems” Zdzisław Papir
ergodicity
ergodicity
Ergodic random signal features that a single signal path represents an ensemble of all signal paths.
Ergodicity of a random signal
Definition of an ergodic random signal:
〈time-averaged moments〉 of a random signal determined for each single signal path are equal to
ensemble (probabilistic) moments calculated for an entire ensemble of signal paths.

## Slide 19
Ergodicity of a mean squared value
1. Paths of a random ergodic signal are power signals (unperiodic) so they do not possess a Fourier transform.
Ergodicity
2. Paths of a random ergodic signal are represented in the frequency domain by a power spectral density and a corresponding autocorrelation function (related by Fourier transform).
„Signals & Systems” Zdzisław Papir
3. Power spectrum density of a random signal can be obtained by ensemble averaging of power density spectra of signal paths.
random process
single path
Power signal

## Slide 20
Spectral analysis of a random signal
„Signals & Systems” Zdzisław Papir
Ad. 2. Paths of a random ergodic signal are represented in the frequency domain by a power spectral density and a corresponding autocorrelation function (by Fourier transform).
Ad. 3. Power spectrum density of a random signal can be obtained by ensemble averaging of power density spectra of signal paths.
Power frequency spectrum of a random signal (averaged over all signal paths) is Fourier transform of an autocorrelation function (averaged over all signal paths).

## Slide 21
„Signal Theory” Zdzisław Papir
Wiener – Chinczyn theorem:
Power spectrum of a stationary random signal is a Fourier transform of its autocorrelation function.
Spectral analysis of a random signal
Note #1: the autocorrelation is to be calculated in the probability domain (pdf of the 2nd order ) instead in the time domain.
Note #2:
pdf of the 1st order describes dispersion of random signal values
pdf of the 2nd order (autocorrelation function) describes power density spectrum of a random signal (after Fourier transformation)

## Slide 22
„Signal Theory” Zdzisław Papir
Spectral analysis of a random signal
Addendum to Wiener – Chinczyn theorem:
Power spectrum of a cyclostationary random process (its autocorrelation function is periodic in t) is a Fourier transform of its time-averaged autocorrelation function (over a period).

## Slide 23: Summary
„Signals & Systems” Zdzisław Papir
Random signal exhibits chaotic fluctuations described by a random variable.
Random signal is an ensemble of deterministic paths which are power signals.
Time averages and ensemble averages are defined for random signals. Ensemble averages do not depend on current time for stationary random signals.
Time averages are equal to enesemble averages for ergodic processes.
Power spectrum of an ergodic random signal is a Fourier transform of its autocorrelation function (Wiener-Chinczyn theorem).

## Slide 24: Case study – amplitude modulation
„Signals & Systems” Zdzisław Papir

## Slide 25: Case study – bipolar NRZ line code
„Signals & Systems” Zdzisław Papir
T
2T
4T
6T
+1
-1
t
x(t)
nT
(n+1)T
an
Symbols an are iid random variables. (iid = independent identically distributed)

## Slide 26
„Signal Theory” Zdzisław Papir
x(t+τ), 0<τ<T
Bipolar NRZ line code - ACF
x(t)
0
T
-T
t
2T
3T
0
T
-T
t
2T
3T
T-
-
2T-
3T-
T
2T
3T
4T
t
+1
2
-T
T-
2T-
3T-




## Slide 27
Bipolar NRZ line code - ACF
„Signal Theory” Zdzisław Papir
T
2T
3T
4T
t
+1
-T
T-
2T-
3T-



2

## Slide 28
„Signal Theory” Zdzisław Papir
Bipolar NRZ line code - ACF
0
T
-T
t
2T
3T
T-
-
2T-
3T-
0
T
-T
t
2T
3T
x(t+τ), τ>T
x(t)
T
2T
3T
4T
t
+1
-T
T-
2T-
3T-
2

## Slide 29: Bipolar NRZ line code – ACF
„Signals & Systems” Zdzisław Papir
T
2T
3T
4T
t
+1
-T

## Slide 30: Bipolar NRZ line code – power spectrum
„Signals & Systems” Zdzisław Papir
f [Hz]
Power spectrum is concentrated in the bandwidth 0 < f < 1/T;
Nyquist theorem (ISI = 0) states that the half of the spectrum 0 < f < 1/(2T) is sufficient (provided synchronous resampling).

## Slide 31: Miller’s line code
„Signals & Systems” Zdzisław Papir
„0”
continuation signal level at transitions „1”  „0”
opposite signal level at transistions „0”  „0”
„1”
maintaining signal level at transitions „1”  „1”
maintaining signal level at transitions „0”  „1”
1
1
0
0
1
1
0
0
0
0
1
1
1

## Slide 32: Miller’s line code
„Signals & Systems” Zdzisław Papir
„1”
„0”
„1”
„1”
„0”
„0”
Miller’s code properties:
reduction of low frequency spectrum components
considerable amount of timing content
spectrum focused in a relatively narrow bandwidth

## Slide 33: Line codes - Miller’s line code
„Signals & Systems” Zdzisław Papir
bipolar NRZ code
Miller’s code