## Slide 1
TRANSMISSION CODES
(LINE CODES)
„Signals @ Systems” Zdzisław Papir

## Slide 2: Agenda
Digital telecommunication system
Natural digital signal (unipolar code)
Properties of transmission codes
Codes: bipolar, biphase, Miller’s
Differential encoding
Pseudoternary codes: AMI & HDB, PRS
Summary
„Signals @ Systems” Zdzisław Papir

## Slide 3: DIGITAL TELECOMMUNICATION SYSTEM
Sampling
Quanti- zation
Encyption (ciphers)
Source coding
Binary coding
Descrambling
Error control coding
Detection
Transmission channel
De- ciphering
Error control decoding
Binary decoding
Pulse formatting
Lowpass filter
Coder
Decoder
„Signals @ Systems” Zdzisław Papir
D/A converter
A/D converter
Scrambling
Source decoding

## Slide 4
„Signals @ Systems” Zdzisław Papir
Analog signal x(t)
Quantized signal v(t)
Signal quantization (8 levels)
0
1
2
3
4
5
Quantization levels
Samples
Quantization thresholds
0 000
3 011
1 001
4 100
5 101
4 100

## Slide 5: A/D converter
„Signals @ Systems” Zdzisław Papir
Information signal is encoded in a binary format in a A/D converter.
Common solution is sampling combined with quantization, and then binary coding of decimal quantization levels.
Sampling at a proper sampling rate does not result in information loss.
Quantization does result in irrertrivable information loss (quantization noise).
Transmission_rate = sampling frequency x codeword_length

## Slide 6: Coder – source coding (compression)
„Signals @ Systems” Zdzisław Papir
Data compression, source coding or bit-rate reduction involves encoding information using fewer bits than the original representation.
Data compression is possible as most of data are redundant so removing some of them does not result in information quality loss.
Compression is useful because it reduces resources required to store and transmit data.
The design of data compression schemes involves trade-offs among various factors, including the degree of compression, the amount of distortion introduced (when using lossy data compression), and the com- putational resources required to compress and decompress the data.

## Slide 7: Compression – taxonomy
„Signals @ Systems” Zdzisław Papir
LOSSLESS COMPRESSION
Run-length coding
Dictionary coding
Entropy coding
LOSSY COMPRESSION (AUDIO, IMAGE, VIDEO)
Discrete Cosine Transform (DCT)
Wavelet compression
Fractal compression
Vector quantization

## Slide 8: Coder – error control coding
„Signals @ Systems” Zdzisław Papir
The general idea for achieving error detection and correction is to add some redundancy (some extra bits) to a message, which receiver can use to check consistency of the delivered message, and to recover data that has been determined to be corrupted.
Error detection/correction codes are increasing the Hamming distance among signals in a signal space.
Two basic schemes of error correction codes: block codes and convolutional codes.
Error correction codes comes in two variants: backward error correction (ARQ – Automatic Repeat Request) and Forward Error Correction (FEC). ARQ combines error detection with requests for retransmission of erroneous data. FEC adds redundancy to enable the receiver to recover the original data.

## Slide 9
Coder - encription
„Signals @ Systems” Zdzisław Papir
Encryption is a transformation of plain (original) data into a cipher. Decryption of a cipher is not possible without a key.
Encryption results in data privacy (confidentiality); secure communications requests implementation of another procedures (autenthication, authorization).
Autenthication – procedure for confirmation a declared identity of an entity taking part in a communication process.
Authorization – procedure checking whether the authenticated entity has been granted an access to requested resources.
Data integrity – procedure guaranteeing that transmitted data have not been altered in communication.
Digital Rights Management – set of access control procedures (based on cryptography techniques) to copyrighted data counteracting their consumption being incompatible with data owner provisions.

## Slide 10: Encryption – cipher taxonomy
„Signals @ Systems” Zdzisław Papir
Historical pen and paper ciphers used in the past are sometimes known as classical ciphers. They include substitution ciphers and transposition ciphers.
During the early 20th century, more sophisticated machines for encryption were used, rotor machines, which were more complex than previous schemes.
Encryption methods can be divided into symmetric key algorithms and asymmetric key algorithms. In a symmetric key algorithm (DES, AES), the sender and receiver must have a shared key set up in advance and kept secret from all other parties; the sender uses this key for encryption, and the receiver uses the same key for decryption.
In an asymmetric key algorithm (RSA), there are two separate keys: a public key is published and enables any sender to perform encryption, while a private key is kept secret by the receiver and enables him to perform decryption.

## Slide 11: Scrambling
Terminal equipment transmits idle codes during user thinking periods (instead of ceasing transmission) in order to keep the required power level and AGC accross network facilities.
The digital stream may be scrambled to provide randomization of the transmitted signal (to facilitate adaptive equalization and timing recovery in the receiver) as long sequences of idle codes do not contain a sufficient amount of timing information.
The simplest form of scrambling is to add a long pseudo-noise (PN) sequence to the data sequence and subtract it at the receiver (via modulo 2 addition); a PN sequence is produced by a Linear Shift Feedback Register (LSFR).
„Signals @ Systems” Zdzisław Papir


data
scrambled data
PN sequence length 2m – 1 = 26 – 1 = 63
PN acf
(2m – 1)T

## Slide 12: Modulator
„Signals @ Systems” Zdzisław Papir
Modulation maps the digital data stream into a form which is suitable for transmission over a physical channel.
Modulation may involve:
  simply translating a sequence of binary digits into a sequence of pulses,
  baseband pulse encoding to 1. combat intersymbol interference, 2. reduce bandwidth, 3. provide timing content and 4. some error resilience,
  mapping a data sequence or baseband pulse sequence onto carrier for placing a signal into the passband of the channel (keying).
8-PSK

## Slide 13: Demodulator
„Signals @ Systems” Zdzisław Papir
Demodulation translates the output of the channel into a digital (binary) format.
Demodulation may involve:
  carrier recovery,
  stripping data sequence from the carrier,
  timing recovery with resampling,
  equalization,
  detection of information.

## Slide 14: DESIRABLE PROPERTIES OF TRANSMISSION CODES
No dc [( = 0) = 0]; dc component is a waste of transmitter power.
Low level power spectrum close to  = 0 as low frequencies are strongly attenuated due to capacity properties of transmission lines.
Narrow bandwidth.
Considerable amount of timing content needed for synchronization between transmiiter and receiver.
„Signals @ Systems” Zdzisław Papir
Line coding maps the digital data stream into electrical symbols which are suitable for transmission over a baseband physical channel.

## Slide 15: NATURAL DIGITAL SIGNAL (unipolar line code)
Assumptions:
Bit duration (clock) T
Signalization rate ωT = 2π/T, fT = 1/T [bps]
Binary signal {0, 1} is a sequence of independent random variables distributed as:
„Signals @ Systems” Zdzisław Papir
x(t)
1
1
1
1
1
1
1
0
0
0
0
T
3T
t
1
0

## Slide 16: Spectrum analysis (unipolar code)
Autocorrelation function (time averaged):
„Signals @ Systems” Zdzisław Papir
Power spectrum:
Neither property 1…4 is met by unipolar code.

## Slide 17: BIPOLAR TRANSMISSION CODE
„Signals @ Systems” Zdzisław Papir
x(t)
1
1
1
1
1
1
1
0
0
0
0
t
-1
1
T
3T
Assumptions:
Bit duration (clock) T
Signalization rate
Binary signal {0, 1} is a sequence of independent random variables distributed as:
ωT = 2π/T, fT = 1/T [bps]

## Slide 18: Spectral analysis (bipolar code)
„Signals @ Systems” Zdzisław Papir
Autocorrelation function (time averaged):
Power spectrum:
Neither property 1…4 is met by bipolar code, though at p = ½ the dc content disappears.

## Slide 19: DIFFERENTIAL PRECODING
„Signals @ Systems” Zdzisław Papir
p = Pr{1}
1 - p = Pr{0}
x’(t)
1
1
1
1
1
1
1
0
0
0
0
t
+1
-1
„0” 1-p
-
+
„1”, p
„1”, p
„0” 1-p
Differential precoding equalizes probability distribution thereby removing dc component.

## Slide 20: BIPHASE LINE CODE
Bipulse
T/2
T
t
r1(t)
1
-1
r0(t)
T/2
T
t
1
-1
„Signals @ Systems” Zdzisław Papir
Remark: power spectrum of a transmission code is proportional to squared a-f spectrum of a pulse.

## Slide 21: Spectrum analysis (biphase code)
Bipolar code
Biphase code
„Signals @ Systems” Zdzisław Papir
Power spectrum:
1
1
1
1
1
1
1
0
0
0
0
2T
T
x(t)
t
1
-1
Bandwidth of biphase code spectrum is 2x greater than a bandwith of a bipolar code due to increased timing content.
Properties 1, 2, and 4 are met; property 3 (bandwidth is not met).

## Slide 22: MILLER’s LINE CODE
„Signals @ Systems” Zdzisław Papir
x(t)
2T
T
t
1
-1
1
1
1
1
1
1
1
0
0
0
0
2T
T
t
1
-1
Biphase code
Miller’s code
+
–
+ –
– +
Miller’s line code:
‘0’ – full pulses
‘1’ – bipulses
signal level unchanged when 1 0
signal level altered when 0  0
Explain the Miller code graph and solve it for p = ½.

## Slide 23: MILLER’s LINE CODE
„Signals @ Systems” Zdzisław Papir
Power spectrum ( = T/2):
Biphase code
Miller’s code
Bipolar code
Miller’s code has:
narrow bandwidth,
no dc component,
low level of low frequencies,
considerable timing content
so properties 1…4 are met.
x(t)
2T
T
t
1
-1
1
1
1
1
1
1
1
0
0
0
0
2T
T
t
1
-1
Biphase code
Miller’s code

## Slide 24: LINE CODE AMI (Alternate Mark Inversion)
„Signals @ Systems” Zdzisław Papir
HDB-3
x(t)
V
1
0
1
1
1
1
V
0
2T
T
t
1
-1
1
-1
AMI
0
0
0
0
0
0
0
0
0
0
0
1
1
t
V
2T
T
B
Line code AMI:
‘0’ – zero level
‘1’ – impulses 1
alternating level at ‘1’
+
0–
0+
–
Explain the graph of the AMI code and solve it for p = ½.
Discuss rules of detection of the HDB-3 code.

## Slide 25: LINE CODE AMI (Alternate Mark Inversion)
Power spectrum:
„Signals @ Systems” Zdzisław Papir
AMI code
Miller’s code
Bipolar code
Biphase code
Bandwidth of AMI code is almost the same as for a bipolar code with low frequencies attenuated (properties 1, 2, and 4 are met).
More timing content is inbuilt in the HDB-3 (High Density Bipolar) code as sequences of 4 zeros („0000”) are eliminated while preserving error resilience.

## Slide 26: PARTIAL RESPONSE SIGNALING (PRS)
„Signals @ Systems” Zdzisław Papir
Power spectra (p = 0.5):
AMI, PRS duobinarny modified
Mille’s code
Bipolar code
Biphase code
PRS duobinarny
PRS duobinary modified
x’(t)
PRS duobinarny
1
0
0
0
0
2T
T
t
1
-1
1
-1
1
1
0
0
0
1
1
0
1
1
1
t
2T
T
x(t) – bipolar code
Bipolar and PRS codes use same pulses though PRS bandwidth is twice narrower.
Duobinary PRS code does not contain low frequencies,
PRS duobinarny
PRS duobinary modified

## Slide 27: PARTIAL RESPONSE SIGNALING (PRS)
„Signals @ Systems” Zdzisław Papir
x’(t)
1
0
0
0
0
2T
T
t
1
-1
1
-1
1
1
0
0
0
1
1
0
1
1
1
t
2T
T
PRS duobinary modified
PRS duobinarny

## Slide 28: SUMMARY
„Signals @ Systems” Zdzisław Papir
Transmission code is a mapping of a binary signal into an electrical signal.
Desired properties of each transmission code: narrow bandwidth, no dc component, low level of low frequencies, and considerable timing content.
Properties of a transmission code may be assessed by its spectral analysis.
Properties of a transmission code may be tuned either by and impulse shape and/or coding rule.
Differential precoding eliminates dc component.