## Slide 1: Signal filtering
„Signals & Systems” Zdzisław Papir
Signal filtering
TILS  RLC filters
Voltage – current relationships for RLC elements
Serial/paralel connection of impedances
Harmonic excitation
Amplitude- and phase-frequency characteristics
Ideal filters – a taxonomy
Signal filtering – Fourier series
Signal filtering – Fourier transform and convolution
How does filtration alter frequency characteristics?
Signal filtering by convolution in time domain
Summary

## Slide 2
„Signals & Systems” Zdzisław Papir
Signal processing in a TILS (RLC networks) needs determination of a transfer function H(s) which depends on an internal structure of an RLC network.
Generic approach to determine the transfer function H(s) is to find an ordinary differential equation (ODE) describing an RLC network (output y(t) in terms of input x(t)), and then „solving” the ODE using a substitution x(t) = est oraz y(t) = H(s)est.
Signal filtering
TILS H(s)
TILS H(s)
Engineering approach to determine the transfer function H(s) is based on some relationships for transfer functions (impedances).

## Slide 3
„Signals & Systems” Zdzisław Papir
R
C
L
any network of RLC elements
Derivation of the TILS transfer function H(s) is supported by various theorems (physics, electrical circuit theory):
voltage/current relationships for R, L, C elements,
Kirchhoff’s Current Law (KCL),
Kirchhoff’s Voltage Law (KVL).
H(s) = ?
RLC Time-invariant Linear Systems
Input signal
x(t)
Output signal
y(t)

## Slide 4
„Sygnały i systemy” Zdzisław Papir
R
C
L
H(s), Z(s), Y(s) = ?
Types of transfer functions
4
Input signal
x(t)
Output signal
y(t)
x(t) | Transfer function | y(t)
current | impedance Z(s) | voltage
voltage | transfer f. v-v H(s) | voltage
voltage | admittance Y(s) | current
current | transfer f. c-c H(s) | current
any network of RLC elements

## Slide 5
„Signals & Systems” Zdzisław Papir
Voltage-current relationships for elements RLC
R
C
L
response (voltage) to exponential excitation
exponential excitation (current)
=
Impedances (current → voltage) for RLC elements

## Slide 6
6
„Signals & Systems” Zdzisław Papir
Impedance vs admittance
Z(s)Y(s) = 1
Y(s) = Z-1(s)
Z(s)
current i(t) = est
voltage u(t) = Z(s)est
impedance
current i(t) = est
1
Y(s)
current i(t) = Y(s)est
admittance
voltage u(t) = est
current i(t) = Y(s)est
2
1
2

## Slide 7
„Signals & Systems” Zdzisław Papir
Serial connection of impedances
Z1(s), Z2(s) – any connection of R, L, C elements
Parallel connection of impedances
Voltage divider (unloaded)

## Slide 8
R
C
x(t)
y(t)
i(t)
i(t)
i(t)
u(t)
„Signals & Systems” Zdzisław Papir
Lowpass RC filter (integrator)
- generic approach

## Slide 9
Lowpass RC filter (integrator)
- engineering approach
R
1/Cs
„Signals & Systems” Zdzisław Papir
x(t)
y(t)

## Slide 10
„Signals & Systems” Zdzisław Papir
Harmonic excitation
H(s:=j)
Filtering does not change frequency; does change amplitude and phase in relation to frequency.

## Slide 11
„Signals & Systems” Zdzisław Papir
Amplitude- and phase- frequency characteristics
Transfer function H(j)
Im
Re
Transfer function H(j)
Polar (exponential) form

## Slide 12: Lowpass filter (LPF) a-f characteristic
„Signals & Systems” Zdzisław Papir
10
-1
10
0
10
1
10
2
10
-4
10
-3
10
-2
10
-1
10
0
log-log amplitude characteristics of the LPF (1st order) (Bode plot)

## Slide 13
decibel [dB] & decade [dec]
„Signal s & Systems” Zdzisław Papir
Two frequencies f1, f2 are spaced by 1 dec
if f1/f2 = 10 so f [Hz]  log10f [dec]
f2 = 1 MHz, f1 = 10 MHz
Two signals with powers P1, P2 are spaced by 1 Bel
(or 10 deciBels) if P1/P2 = 10.
P1/P2 = 10  log10P1/P2 = 1 B or 10log10P1/P2 = 10 dB
10log10S/N = SNR [dB]
Signal to Noise Ratio
Comparing voltages U1, U2 needs the formula 20log10U1/U2.

## Slide 14
„Signals & Systems” Zdzisław Papir
Ideal filters – a taxonomy
RLC filters are analog circuits which perform signal spectrum shaping, specifically:
to remove unwanted frequency components or/and
to emphasize wanted frequency components.
Original signal spectrum
Lowpass
Filtering (LPF)
Highpass
filtering
Stopband
filtering
Bandpass
Filtering (BPF)
f [Hz]
f [Hz]
f [Hz]
f [Hz]
f [Hz]
Emphasize
filtering
f [Hz]
Types of ideal filters H(f):
Two important properties of ideal filters:
brickwall shaped edges
full stopband
These properties are not attainable with R, L, C elements according to the Paley-Wiener condition.

## Slide 15
The Fourier series of the output signal y(t)
Signal filtering – Fourier series
„Signals & Systems” Zdzisław Papir

## Slide 16: Sawtooth input signal x(t)
0
0.5
1
1.5
2
2.5
3
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Sawtooth signal (period T)
time t/T
x(t)
Signal filtering - example
„Signals & Systems” Zdzisław Papir

## Slide 17: Lowpass filter (integrator)
R
1/Cs
„Signals & Systems” Zdzisław Papir
x(t)
y(t)

## Slide 18: Input/output signals – Fourier series
„Signals & Systems” Zdzisław Papir

## Slide 19: Output signal y(t) (fb/f0 = 9)
0
0.5
1
1.5
2
2.5
3
3.5
0
0.2
0.4
0.6
0.8
1
Lowpass filter response
time t/T
fb/f0 = 9
„Signals & Systems” Zdzisław Papir

## Slide 20: Output signal y(t) (fb/f0 = 3)
0
0.5
1
1.5
2
2.5
3
3.5
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Lowpass filter response
time t/T
fb/f0 = 3
„Signals & Systems” Zdzisław Papir

## Slide 21: Output signal y(t) (fb/f0 = 1)
0
0.5
1
1.5
2
2.5
3
3.5
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Lowpass filter response
time t/T
fb/f0 = 1
„Signals & Systems” Zdzisław Papir

## Slide 22: Output signal y(t) (fb/f0 = 1/3)
0
0.5
1
1.5
2
2.5
3
3.5
0.4
0.45
0.5
0.55
0.6
0.65
0.7
0.75
Lowpass filter response
time t/T
fb/f0 = 1/3
„Signals & Systems” Zdzisław Papir

## Slide 23
Fourier transform of an output signal y(t)
Signal filtering - Fourier transform
Fourier transform Y(jω) of an output signal of a filter y(t) is equal to a product
of Fourier transforms H(jω) X(jω) where h(t)↔ H(jω) and x(t)↔ X(jω) .
„Signals & Systems” Zdzisław Papir

## Slide 24
Signal filtering – example
(Fourier approach)
„Signals & Systems”  Zdzisław Papir

## Slide 25
Sinus integral properties
„Signals & Systems”  Zdzisław Papir
1. Sinus integral is an odd function
2. Sinus integral in zero vicinity (x  0)

## Slide 26
Sinus integral properties
„Signals & Systems”  Zdzisław Papir
3. Horizontal asymptote (x )
4. Local extrema

## Slide 27
Lowpass filtering sgn(t) – output signal
„Signals & Systems”  Zdzisław Papir
+1
-1
0

## Slide 28
Lowpass filtering sgn(t) – slope rising time
„Signals & Systems”  Zdzisław Papir
Slope rising time is inversely proportional to a filter bandwidth.
+1
-1
+/W
-/W
tr = 2/W = 1/B
0

## Slide 29
Lowpass filtering sgn(t) – Gibbs effect
„Signals & Systems”  Zdzisław Papir
+1
-1
+/W
0
Peak value od the output signal is independent of the filter bandwidth (Gibbs effect).

## Slide 30
Signal filtering - convolution
„Signals & Systems”  Zdzisław Papir
Output signal of a filter is a convolution
of input signal and an impulse response of a filter.

## Slide 31
Signal filtering – example
(convolution approach)
„Signals & Systems”  Zdzisław Papir

## Slide 32
Summary
„Signals & Systems” Zdzisław Papir
The response of Time-Invariant Linear System (TILS) to a composite input is a sum of responses to individual input components.
The exponential signal is an invariant to Linear
Time-invariant Systems (TILS).
Fourier series and Fourier transform represent a signal through its spectrum which is a linear combination of exponential signals.
Fourier series is suited for periodic signals while Fourier transform is suited for unperiodic signals.
Signal filtering is described either in the frequency domain (multiplication of spectra) or in the time domain (convolutrion).

## Slide 33
Kirchhoff laws in RLC networks
„Signals & Systems” Zdzisław Papir
VS
Kirchhoff Voltage Law
CS
RLC network (example)
CS – current source of predefined profile i(t)
VS – voltage source of predefined profile v(t)
Kirchhoff Current Law
any RLC element

## Slide 34
Kirchhoff Current Low (KCL)
„Signals & Systems” Zdzisław Papir
The algebraic sum of currents in an electrical network meeting at a node is zero.
Note that current is a signed (positive or negative) quantity reflecting direction towards or away from a node.
The sum of currents flowing into that node is equal to the sum of currents flowing out of that node

## Slide 35
Kirchhoff Voltage Low (KVL)
„Signals & Systems” Zdzisław Papir
The algebraic sum of voltage drops and voltage sources around any closed electrical loop is zero.
By agreement, voltage drop is a negative quantity while voltage source is a positive quantity.
VD
VS
VD
VD
VD

## Slide 36
„Signals & Systems” Zdzisław Papir
Preemphasis filter
R
1/Cs
r << R
x(t)
y(t)
A preemphasis filter at a transmitter (together with an accompanying deemphasis filter at a receiver) provide better noise immunity in both radio and television broadcasting.

## Slide 37
Preemphasis filter – transfer function – generic approach
„Signals & Systems” Zdzisław Papir

## Slide 38
Preemphasis filter – transfer function – engineering approach
„Signals & Systems” Zdzisław Papir
1/Cs

## Slide 39
Preemphasis filter – a-f characteristic
R
1/Cs
r
x(t)
y(t)
„Signals & Systems” Zdzisław Papir

## Slide 40
Preemphasis filter (a-f characteristic)
„Signals & Systems” Zdzisław Papir
Log-log amplitude – frequency characteristic
10
0
10
1
10
2
10
3
10
4
10
-2
10
-1
10
0
log10f [dec]
20log10H(f) [dB]
Preemphasis filter
f2/f1 = 100 = 2 dec
Asymptotic amplitude Bode plot
f1
f2

## Slide 41
Problems