## Slide 1
Noise in transmission systems
„Signals & Systems” Zdzisław Papir
Transmission System
Noise vs. impairments
Noise sources in a transmission system
Additive White (Wideband) Gaussian Noise
Filtering AWGN
Noise in transmission systems
Additive Narrowband Gaussian Noise - model
Summary

## Slide 2
Transmission System
„Signals & Systems” Zdzisław Papir
TRANSMITTER
RECEIVER
TRANSMISSION CHANNEL
noise & impairments
filtering &
modulation
filtering &
detection

## Slide 3
Noise vs. Impairments
„Signals & Systems” Zdzisław Papir
Noise is a random fluctuation in an electrical signal and it can be produced by several different effects. Noise is a summation of unwanted or disturbing energy from natural sources.
Impact of noise can be minimized to some extent.
Noise is distinguished from impairments like:
electromagnetic interference from other transmitters,
distortion being an unwanted systematic alteration of the signal waveform by the communication equipment (nonlinearity, fading, dispersion).
Impairments can be (almost) completely eliminated.

## Slide 4
Noise sources in a transmission system
„Signals & Systems” Zdzisław Papir
Two broad classes of noise sources:
external to the system,
internal to the system.
External noise sources:
  atmospheric noise,
  solar noise,
  cosmic noise.
Internal noise sources:
  thermal noise (sz. termiczny),
  shot noise (sz. śrutowy),
  generation-recombination noise,
  flicker noise (sz. migotania),
  quantum noise (sz. kwantowy).
„Signals & Systems” Zdzisław Papir

## Slide 5
Thermal noise
„Signals & Systems” Zdzisław Papir
„Signals & Systems” Zdzisław Papir
1. Thermal noise (Nyquist noise) is the electronic noise generated by the thermal excitation of the charge carriers (usually the electrons) inside an electrical conductor which happens regardless of any applied voltage.
3. Thermal noise power spectrum is flat (white) up to frequencies of 1000 GHz = 1 THz (at T = 290 degK= 17 degC).
2. Thermal noise amplitudes are assumed to be governed by a Gaussian (normal) pdf. The assumption is justified by the central-limit theorem as the noise is a result of random motion of a large number of charge carriers.
4. Thermal noise is assumed to be added to signals transmitted over a channel.
4 & 3 & 2 & 1 = Additive White Gaussian Noise (AWGN)
White = Wideband

## Slide 6
Additive White Gaussian Noise
TRANSMISSION CHANNEL
AWGN z(t)
signal
signal + z(t)
Additive
„Signals & Systems” Zdzisław Papir
White
~1000 GHz

## Slide 7
Additive White Gaussian Noise
„Signals & Systems” Zdzisław Papir

## Slide 8
80 dBm 100 kW Typical transmission power of FM radio station
50 dBm 100 W Typical thermal radiation emitted by a human body
0 dBm 1 W Typical RF leakage from a microwave oven
− 80 dBm 10pW Typical range of wireless received signal power
−106 dBm Analog television channel
−127.5 dBm Typical received signal power from a GPS satellite
−134 dBm AWGN in a 10 kHz bandwidth
−174 dBm AWGN in a1 Hz bandwidth
Power in dBm – some examples

## Slide 9
-4
-3
-2
-1
0
1
2
3
4
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
„Signals & Systems” Zdzisław Papir
Gaussian
Distribution
Additive White Gaussian Noise

## Slide 10
Filtering AWGN
„Signals & Systems” Zdzisław Papir
Any filter H()
Any kind of filtering does preserve the Gaussian form of p.d.f.s.
AWGN, z(t)
Gaussian noise, n(t)

## Slide 11
Filtering AWGN
Ideal low (ILPF)- or bandpass (IBPF) filter H()
„Signals & Systems” Zdzisław Papir
ILPF
IBPF
ANGN, n(t)
(narrowband)
AWGN, z(t)
(wideband)

## Slide 12
„Signals & Systems” Zdzisław Papir
TRANSMITTER
RECEIVER
TRANSMISSION CHANNEL
AWGN Additive Wideband GN
modulation
detection
Noise in transmission systems

## Slide 13
Transmitter
„Signals & Systems” Zdzisław Papir
ILPF
MOD
IBPF
Information signal
Modulated signal
ILPF – Ideal Lowpass Filter (bandlimiting of information signal)
IBPF – Ideal Bandpass Filter (removing out-of-band frequencies)
MOD – Modulator (shifting information signal into channel bandwidth)
x(t) – information signal, bandwidth m
(t) – modulated signal, bandwidth W > m
c(t) – harmonic carrier, frequency 0 >> m
Carrier

## Slide 14
Receiver
„Signals & Systems” Zdzisław Papir
IBPF
DEMOD
ILPF
Information signal
Modulated signal
LPF – (Ideal) Lowpass Filter (removing out-of-band frequencies)
BPF – (Ideal) Bandpass Filter (removing out-of-band noise)
DEMOD – Demodulator (stripping information signal from the received signal)
Carrier

## Slide 15
Stereo sound FM: B = 200 kHz, f0  100 MHz, B/f0 = 0,002
CATV: B = 8 MHz, f0  500 MHz, B/f0 = 0,016
SAT TV: B = 40 MHz, f0  4 GHz, B/f0 = 0,01
Fiber transmission: III window 1550 nm ~ 200 THz!, window bandwidth 30 nm, B/f0 = 0,02
Narrowband signals
„Signals & Systems” Zdzisław Papir

## Slide 16
„Signals & Systems” Zdzisław Papir
ILPF
MOD
IBPF
SNR in transmission systems
IBPF
DEMOD
ILPF
Signal to Noise Ratio
ANGN – Additive Narrowband GN
Transmission channel

## Slide 17
„Signals & Systems” Zdzisław Papir
IBPF
DEMOD
ILPF
Modulation gain – measure of noise immunity
g – output SNRO delivered by unit input SNRI and unit system relative bandwidth .

## Slide 18
Passband vs. Baseband System
„Signals & Systems” Zdzisław Papir
ILPF
MOD
IBPF
ILPF
DEMOD
ILPF
Modulation gain is a measure how much a passband system is „better” or „worse” than a baseband system in terms of SNRs.
Transmission channel

## Slide 19
Noise Characteristics
„Signals & Systems” Zdzisław Papir
Signal to noise ratio γ of a modulated signal PI to noise N present in a bandwidth ωm of a modulating signal. Note that there is no point in the system with such an SNR.

## Slide 20
Noise Characteristics
baseband (g = 1)
passband (g > 1) – modulation gain
passband (g < 1) – modulation loss
g[dB]
g[dB]
„Signals & Systems” Zdzisław Papir
More effects will appear:
threshold in noise characteristcs
SNR - bandwidth tradeoff

## Slide 21
„Signals & Systems” Zdzisław Papir
Additive Narrowband Gaussian Noise (ANGN)
ANGN sample path
amplitude & frequency fluctuations

## Slide 22
„Signals & Systems” Zdzisław Papir
ANGN - Lowpass Representation
IBPF
Wideband Gaussian Noise (AWGN)
Narrowband Gaussian Noise (ANGN)
AWGN, 
ANGN

## Slide 23
ANGN – phasor diagram
„Signals & Systems” Zdzisław Papir
quadrature component
jnQ(t)
nI(t)
n(t)
t = const
inphase component
Both inphase and quadrature processes are modeled by a Gaussian i.i.d. r.v. which summation on the complex plane provides both
amplitude and frequency (phase) random variations.

## Slide 24
1
2
n = 10
n = 100
n = 1000
„Signals & Systems” Zdzisław Papir
ANGN – phasor diagram

## Slide 25
„Signals & Systems” Zdzisław Papir
ANGN component spectra
(double sideband case)

2

## Slide 26
ANGN – double sideband case – power budget

2
„Signals & Systems” Zdzisław Papir

## Slide 27
„Signals & Systems” Zdzisław Papir


ANGN component spectra (single sideband case)

## Slide 28
Summary
„Signals & Systems” Zdzisław Papir
Additive White Gaussian Noise:
simply adds to the information carrying signals
has a flat spectrum across all frequencies
fluctuates according to the normal p.d.f. (mean-squared variation = noise power)
does not change its probabilistic nature when filtering (LPF, BPF)
is modeled as a superposition of lowpass (inphase, quadrature) components which mimic both amplitude and frequency fluctuations